Section Cover Page

Section 02 41 20 2014-11-01 Interior Demolition

Use this section only to specify requirements for partial, non structural demolition of interior building walls, partitions, finishes, equipment and fittings as would be required for an interior renovation project.  It is not suitable for exterior selective demolition or demolition and disposal of entire buildings or structures.

This Master Specification Section contains:

.1	This Cover Page

.2	Data Sheet - General

.3	Specification Section Text:

1.	General

1.1	Related Work Specified in Other Sections

1.2	Reference Documents

1.3	Submittals

1.4	Existing Conditions

1.5	Protection

1.6	Temporary Partitions

1.7	Salvageable and Recyclable Materials

- Products

2.1	Materials and Equipment

3.	Execution

3.1	Materials To Be Retained By Province

3.2	Materials To Be Reused

3.3	Demolition

3.4	Existing Services

3.5	Restoration

3.6	Clean Up

Asbestos Materials:

Prior to demolition of any portion of a structure that has known quantities of asbestos, the portion of the building must be decontaminated of all asbestos materials, which may involve the following special procedures:

.1	Isolation and Preparation.

.2	Special Equipment Requirements.

.3	Special Enclosure of Area.

.4	Sealing of Material.

.5	Removal of Material.

.6	Clean-up of Area prior to other work.

Obtain information about special procedures and requirements peculiar to each asbestos condition from Infrastructure.

Refer to Sections 02 82 01, 02 82 05, 02 82 15, 02 82 33, 02 84 16 and 02 84 25 of the Basic Master Specification.

Existing Information:

Available working drawings, detail drawings, and photographs applicable to the areas of demolition work should be included for information purposes only.  Refer to Section 00 31 00, Available Project Information.

1.	General

1.1	RELATED SECTIONS

.1	Scheduling of work:	Division 01.

.2	Submittals:	Section 01 33 00.

.3	LEED Requirements	Section 01 35 18.

.4	Temporary Facilities and Controls:	Section 01 50 00.

.5	Waste Management and Disposal	Section 01 74 19.

1.2	REFERENCE documents

.1	American National Standards Institute (ANSI):

| .1 | ANSI A10.8-2001 | Safety Requirements for Scaffolding |
| --- | --- | --- |

.2	Canada Green Building Council (CaGBC):

| .1 | LEED Canada 2009 Rating System | LEED Canada for New Construction and Major Renovations. LEED Canada for Core and Shell Development. Website: www.cagbc.org] |
| --- | --- | --- |

.3	Canadian Standards Association (CSA):

| .1 | CSA S350-M1980 (R2003) | Code of Practice for Safety in Demolition of Structures |
| --- | --- | --- |

.4	Hazardous Materials Information Review Act, 1985

.5	Motor Vehicle Safety Act (MVSA), 1995

.6	National Fire Protection Association (NFPA):

| .1 | NFPA 241-04 | Standard for Safeguarding Construction, Alteration, and Demolition Operations |
| --- | --- | --- |

1.3	submittals

.1	Prior to beginning of Work on site submit detailed Waste Reduction Workplan in accordance with Section 01 74 19 and indicate:

.1	Descriptions of and anticipated quantities [in percentages] [          ] of materials to be salvaged  reused, recycled and landfilled.

.2	Schedule of selective demolition.

.3	Number and location of dumpsters.

.4	Anticipated frequency of tippage.

.5	Name and address of [haulers] [waste facilities] [waste receiving organizations].

1.4	EXISTING CONDITIONS

.1	Visit and examine the site and note all characteristics and irregularities affecting the work of this Section.

1.5	PROTECTION

.1	Take precautions to guard against damage to adjacent work.  Be liable for any damage or injury caused.

.2	Cease operations and notify Province if safety or any adjacent work appears to be endangered.  Do not resume operations until reviewed with the Province.

.3	Ensure safe passage of building occupants around and through area of demolition.

.4	Cease operations and notify the Province immediately for special protective and disposal instructions when asbestos materials or other hazardous materials [, other than those identified,] are uncovered during the work of this project.

.5	Protect temporarily suspended work that is without continuous supervision to prevent access by unauthorized persons.

1.6	TEMPORARY PARTITIONS

SPEC NOTE:  This article is required only on extensive renovations where an affected section of the building can be closed off.  Consider extent of renovation work areas.  Delete if not required.  Avoid duplication of requirements specified in Division 01.

.1	Erect and maintain dustproof partitions, seal off ducts as required to prevent spread of dust and fumes to other parts of the building.  On completion, remove partitions and make good surfaces to match adjacent surfaces.

1.7	SALVAGEABLE AND RECYCLABLE MATERIALS

.1	Except where otherwise specified, all materials indicated or specified to be permanently removed from the Place of the Work shall become Contractor's property.  Maximize to the fullest extent possible, salvage and recycling of such materials, consistent with proper economy and expeditious performance of the Work.

.2	To reduce the quantity of material otherwise destined for disposal at a landfill, the Contractor is encouraged to consider utilizing the services of businesses and non-profit organizations that specialize in salvage and recycling of used building materials, but does so at his own option and risk

.3	A current listing of recyclers specializing in specific categories of materials may be obtained during normal office hours from:

Alberta Environment

Recycling Branch

Recycle Info Line

Phone:  (780) 427-6982 or 1-800-463-6326

Website:www.recyclinghotline.ca

2.	Products

  - Materials and Equipment

.1	Provide materials and equipment as required to perform the work of this section.

3.	Execution

3.1	MATERIALS TO BE RETAINED BY PROVINCE

.1	Relics and antiquities, commemorative plaques, and tablets, and similar objects remain the property of the Province of Alberta and shall be [protected] [packaged] [shipped to] [turned over to] [                        ].

SPEC NOTE:  Define special items and requirements.

.2	Carefully remove the following materials and equipment from [Room No.     ] [          Area] to be retained by the [Province] [Owner].  Obtain instructions from [                    ] regarding delivery arrangements of such materials to [                                    ].

SPEC NOTE:  Define and list fixtures, materials and equipment, and indicate locations of items.  Define any special items or special circumstances.

3.2	MATERIALS TO BE REUSED

.1	Carefully remove, store and protect for re installation by Section [              ] the following material and/or equipment:

.1	Light fixtures [and ballasts].

.2	Electrical panels.

.3	Electrical switch gear and controls.

.4	Boiler [and heat exchanger].

.5	Radiant convectors.

.6	Sheet metal ducting.

.7	Ceiling and wall registers and diffusers.

.8	Facebrick, cleaned and made ready for re use.

.9	Windows and glass.

.10	Doors and hardware.

.11	Cabinet work and fitments.

.12	Miscellaneous or ornamental metals.

.13	Metal [toilet] partitions [and screens].

.14	Demountable partitions.

.15	Mirrors.

.16	Shelving.

.17	Equipment   [Mechanical] [Electrical] [Kitchen] [Laundry] [Vending] [Athletic] [Lavatory].

SPEC NOTE:  Above list is outline only.  Complete list accurately as required and indicate new locations of items.  Coordinate and repeat clause for each applicable section of specifications.

3.3	DEMOLITION

.1	Unless otherwise specified, carry out demolition in accordance with CSA S350.

.2	Completely demolish the items scheduled and immediately remove materials from the premises.

.3	Carry out demolition work in a manner to least inconvenience adjacent occupied building area.

.4	Carry out demolition in an orderly and careful manner.

.5	Lower waste materials in a controlled manner; do not drop or throw materials from heights.

3.4	EXISTING SERVICES

.1	Disconnect all electrical and telephone service lines in the areas to be demolished.  Post warning signs on all electrical lines and equipment which must remain energized to serve other areas during period of demolition.  Disconnect electrical and telephone service lines in demolition areas to the requirements of local authority having jurisdiction.

.2	Disconnect and cap all mechanical services in accordance with requirements of local authority having jurisdiction.  Natural gas supply lines shall be removed by the gas company or by a qualified tradesman in accordance with gas company instructions.

SPEC NOTE:  Coordinate utility demolition work with Divisions 20 to 25 and 26 as required.

.3	Essential Services:  Maintain fire alarm and all essential services to [the following] [all] areas:  [          ] [          ].

SPEC NOTE:  If essential services must be interrupted, specify shutdown times in Division 01.  Edit above clause to suit.

.4	In each case notify the affected utility company in advance and obtain approval where required, before commencing with the work on main services.

3.5	RESTORATION

.1	Make good any demolition to the existing work beyond that necessary for carrying out new work, at no expense to the Province.

3.6	CLEAN UP

.1	Remove all debris and rubbish away from site at regular intervals.

.2	Remove all tools and equipment from site.

END OF SECTION