Section Cover Page

Section 02 92 19 Removal and Disposal of 2024-06-18 Mercury Components

Use this section to specify the removal and disposal of mercury components.

This Section may be used as part of a renovation contract or as part of a contract directly with a hazardous waste disposal contractor.  Edit this Section to suit contracting option selected.

This Technical Specification Section contains:

.1	This Cover Sheet

.2	Specification Text

1.	General

1.1	Section Includes

1.2	Removal Contractors Qualifications

1.3	Disposal Contractor Qualifications

1.4	Regulatory Requirements

2.	Products

Not Used

3.	Execution

3.1	Mercury-Containing Equipment

1.	General

1.1	SECTION INCLUDES

.1	This Section includes requirements for identification removal, preparation for disposal, transportation, and permanent disposal of mercury components.

1.2	REMOVAL CONTRACTOR QUALIFICATIONS

.1	Use qualified electrician for removal, packaging and transportation arrangements for disposal of mercury-containing switches, thermostats and equipment.

1.3	DISPOSAL CONTRACTOR QUALIFICATIONS

.1	Handling and transportation of mercury components shall be performed by a hazardous waste company in compliance with the Environmental Protection and Enhancement Act.

.2	Carrier of hazardous wastes shall have successfully completed a Transportation of Dangerous Goods course acceptable to the authority having jurisdiction within the past three years.

1.4	REGULATORY REQUIREMENTS

.1	Comply with the following:

.1	Environmental Protection Act, (1999) (Canada).

.2	Environmental Protection and Enhancement Act, (2023) (Alberta).

.3	Transportation of Dangerous Goods Act, (1992) (Canada).

.4	Dangerous Goods Transportation and Handling Act (2021) and Regulations (1997) (Alberta)

.5	Other legislation and regulations which apply to the performance of asbestos control work.

2.	Products (Not Used)

3.	Execution

3.1	Mercury-Containing Equipment

.1	Locate and remove mercury-containing switches, thermostats and equipment designated to be disposed of.

.2	Place all mercury-containing components into an impervious container packed with absorptive material.

3.5	TRANSPORTATION AND PERMANENT DISPOSAL

.1	Transport waste mercury components in accordance with the Alberta and Federal legislation and regulations.

.2	Ensure that all materials are properly packaged and labeled prior to transportation.

.3	Transport hazardous waste materials in properly placarded vehicles.

.4	Each load shall be accompanied by a properly completed Transportation of Dangerous Goods Regulation (TDGR) Waste Manifest.  Provide the [Province] [Environmental Consultant] with a copy of each shipping and waste manifest.

.5	Use an approved hazardous waste company to transport and permanently dispose of mercury-containing components.

END OF SECTION