Section Cover Page

Section 02 95 00 2024-06-18 Removal and Disposal of Biohazards

Use this section to specify procedures and personal protection requirements for the removal and disposal of accumulated bird excrement (primarily pigeon droppings) and dead animals.  This is an interim section that may be used on projects.

This Section may be used as part of a renovation contract or as part of a contract directly with a hazardous waste disposal contractor.  Edit this Section to suit contracting option selected.

This Technical Specification Section contains:

.1	This Cover Sheet

.2	Specification Text

1.	General

1.1	Intent

1.2	Worker Protection

2.	Products

2.1	Materials

3.	Execution

3.1	Cleaning

3.2	Final Cleaning

3.3	Protective Clothing Disposal and Cleaning

3.4	Disposal of Biohazard Waste

1.	General

1.1	intent

.1	This Section specifies procedures and personal protection requirements for the removal and disposal of accumulated bird excrement (primarily pigeon droppings), rodent droppings and dead animals.

1.2	worker protection

.1	Provide workers with NIOSH approved half-face negative pressure respirators equipped with combination organic vapour / P100 filter cartridges, disposable coveralls c/w hoods, goggles, rubber gloves and safety toed rubber boots.

2.	Products

2.1	MATERIALS

.1	Plastic Bags:  minimum 150 micrometers thick polyethylene.

.2	10% bleach solution: 235 mL bleach to 5 litres water.

.3	Non-powered half mask respirator equipped with P100 filters (minimum).

.4	Protective gloves (polyvinyl chloride or latex).

.5	Disposable or cloth coveralls.

.6	Rubber boots or easily decontaminated footwear.

.7	Eye protection.

3.	Execution

3.1	Cleaning

.1	Wet all material with 10% bleach solution to minimize the airborne dust level during removal.

.2	Shovel excrement and carcasses into plastic bags.  Seal bags with tape.

3.2	final cleaning

.1	Spray all floor areas with a 10% bleach solution at completion of removal.

3.3	Protective Clothing Disposal and Cleaning

.1	At completion of work:

.1	Dispose of protective clothing as biohazard waste.

.2	Wash goggles, rubber gloves, rubber boots, and exterior surface of respirator, with a 10% bleach solution, and rinse with water.

3.4	Disposal OF BIOHAZARD WASTE

.1	Dispose of biohazard waste (bird excrement, rodent droppings, animal carcasses, disposable protective clothing, etc.) in sealed plastic bags at a secured land fill site.

END OF SECTION