Section Cover Page

Section 09 24 23 2014-11-01 Portland Cement Stucco

Delete LEED items if project: .1 is excluded by the Department’s policy on LEED, or .2 the Department has determined that the work of this Contract is not to attain a LEED rating.

Use this master specification to specify stucco (exterior portland cement plaster).

This Master Specification Section contains:

.1	This Cover Sheet

.2	Specification Section Text:

1.	General

1.1	Related Sections

1.2	Reference Documents

1.3	Requirements

1.4	Submittals

1.5	Quality Assurance

1.6	Delivery, Storage, and Handling

2.	Products

2.1	Materials

2.2	Mixing and Proportioning

3.	Execution

3.1	Preparation of Surfaces

3.2	Application

  - Finish Colour and Texture

3.4	Control Joints

3.5	Expansion Joints

3.6	Curing

1.	General

1.1	RELATED SECTIONS

.1	[LEED Submittal Forms	Section 01 32 16]

.2	[LEED Requirements	Section 01 35 18]

.3	[Environmental Procedures	Section 01 35 20]

.4	Waste Management and Disposal	Section 01 74 19.

.5	Furring and Lathing for Plaster:	Section 09 22 10.

1.2	refernce documents

.1	American Society for Testing and Materials (ASTM):

| .1 | ASTM C932-06 | Surface-Applied Bonding agents for Exterior Plastering |
| --- | --- | --- |

.2	Association of Wall and Ceiling Contractors (AWCC):

| .1 | Association of Wall and Ceiling Contractors Specification Standards Manual", 2003 Edition, Section 9.3 – Stucco (AWCC Manual) |
| --- | --- |

.3	Canada Green Building Council (CaGBC):

| .1 | LEED Canada 2009 Rating System | LEED Canada for New Construction and Major Renovations. LEED Canada for Core and Shell Development. Website: www.cagbc.org |
| --- | --- | --- |

.4	Canadian General Standards Board (CGSB):

| .1 | CAN/CGSB-51.32-M77 | Sheathing, Membrane, Breather Type |
| --- | --- | --- |

.5	Canadian Standards Association (CSA):

| .1 | CSA-A8/A5/A362-93 | Portland Cement / Masonry Cement / Blended Hydraulic Cement |
| --- | --- | --- |

1.3	Requirements

.1	Comply with "Association of Wall and Ceiling Contractors Specification Standards Manual", 2003 Edition, Section 9.3 – Stucco. (AWCC Manual).

1.4	submittals

.1	Product Data:

.1	Submit manufacturer’s printed product literature, specifications and data sheets in accordance with Section 01 33 00 - Submittal Procedures.

.2	Provide data from manufacturer of liquid bonding agent indicating compliance with requirements.

.3	Submit [two] [         ] copies of Workplace Hazardous Materials Information System (WHMIS) Material Safety Data Sheets (MSDS) in accordance with Section [01 33 00 - Submittal Procedures] [         ]. Indicate VOCs.

.2	Samples:

.1	Comply with requirements of Division 01.

.2	Submit duplicate 300 x 300 mm samples of specified finish for approval by Province.

1.5	quality assurance

.1	Mock-Ups:

SPEC NOTE:  Specify Site Mock-up in lieu of samples if samples will not adequately establish standard of finish texture.

.1	Prepare minimum 1200 mm x 2400 mm site mock-up showing specified finish and thickness of each coat, for approval by Province.

.2	Approved mock-up shall establish minimum standard for work of this Section.

1.6	Delivery, Storage, and handling

.1	Waste Management and Disposal:

.1	Separate waste materials for [reuse] [and] [recycling] in accordance with Section 01 74 19 – Management and Disposal.

2.	Products

2.1	MATERIALS

.1	Sheathing Paper:  to CAN/CGSB-51.32, breather type.

.2	Trim accessories:  in accordance with AWCC Manual.

.3	Reinforcement:  metal lath or stucco mesh in accordance with AWCC Manual.

.4	Portland Cement:  to CAN/CSA-A5 [white] [grey].

.5	[Sand] [Lightweight Aggregate] [White Sand] and Water:  in accordance with AWCC Manual.

.6	Colour Additive:  Non-fading mineral pigments.

.7	Liquid Bonding Agent:  to ASTM C932, non-re-emulsifiable.  Suitable for incorporation into plaster mix.

.8	Stone:

.1	Type:  [Dolomite][Marble][Quartzite].

.2	Size:  [in accordance with AWCC Manual][            ].

.3	Colour:  as selected by Province from standard range.

SPEC NOTE:  Delete Stone if not applicable.  For guidance on chip size, see chip size list in TTMAC Spec Study on Terrazzo (Portland Cement).  Consult with local suppliers to establish availability.

2.2	MIXING AND PROPORTIONING

.1	Mix and proportion stucco in accordance with AWCC Manual.

3.	Execution

3.1	PREPARATION OF SURFACES

.1	Prepare surfaces in accordance with AWCC Manual.

3.2	APPLICATION

.1	Apply materials in accordance with AWCC Manual.

.2	Apply sheathing paper horizontally.  Lap side joints 100 mm and ends 200 mm, to drain to exterior.

3.3	FINISH COLOUR AND TEXTURE

.1	Texture:	[Sand finish].

[Trowel-textured:  texture and design as selected by Province].

[Brush dash:  [fine][coarse][, knock-down stucco texture]].

[Wet dash:  with stone as specified].

[Dry dash:  with [stone][white sand third coat] as specified].

[Machine spray:  [fine][coarse][, knock-down stucco texture]].

.2	Colour:  [       ] [as selected by Province].

.3	Match [sample] [site mock-up] approved by Province.

3.4	CONTROL JOINTS

.1	Provide control joints consisting of back-to-back plaster stops, 6 mm apart, in the following locations:

.1	At maximum 3.0 m centres for exterior surfaces.

.2	Over junction of structural members and nonstructural members.

.3	Over control joints in block walls.

.4	At line of door jambs from top of door frame to top of stucco or first horizontal joint above door.

.5	As indicated on drawings.

.2	Install control joints straight, true and rigid.

3.5	EXPANSION JOINTS

SPEC NOTE:  Ensure expansion joints are detailed and locations indicated on drawings.

.1	Provide expansion joints as detailed on drawings.

.2	Provide expansion joints at all building expansion and construction joints, and where indicated on drawings.  Install straight, true and rigid.

3.6	CURING

.1	Moist cure as required to prevent shrinkage and drying before hydration and hardening of stucco takes place.

.2	Provide tarpaulins as required to prevent excessive drying in hot and windy conditions.

END OF SECTION