Section Cover Page

Section 09 68 19 2022-04-21 Modular Carpet

Refer to “Green Building Notes” page for additional guidance for projects following a sustainable rating system. Revise Green Building requirements if the Province has determined that the work of this Contract is not to attain a sustainable rating system certification.

This Section specifies modular carpet based on a standard established by Alberta Infrastructure (the Department) for modular carpet in Government of Alberta space (owned and leased).

This Master Specification Section contains:

.1	This Cover Page

.2	Green Building Notes

.3	Specification Section Text:

1.	General

1.1	Related Requirements

1.2	Reference Standards

1.3	Product Options and Substitutions

1.4	LEED Requirements

1.5	Submittals (Tile Layout and Samples)

1.6	Maintenance Materials

1.7	Environmental Requirements (Conditions)

1.8	Removal of Existing Carpet Tile, Adhesive & Waste Removal

1.9	Product Handling, Delivery & Storage

1.10	Warranty

1.11	Project Conditions

1.12	Coordination

2.	Products

2.1	Material Components

2.2	Accessories

2.3	Resilient Base

3.	Execution

3.1	Examination (Condition of Substrate)

3.2	Preparation

3.3	Installation

3.4	Installation At Outlet Boxes/Floor Access Panels

3.5	Installation of Resilient Base

3.6	Cleaning and Protection

3.7	Training

Green Building Notes:

If the project is not designated to use a sustainable rating system it is still be prudent to leave in relevant green building requirements as part of an effort towards sustainability.

Review and incorporate requirements from the following document into the project:

Section 1.0 “Sustainability” of the “Technical Design Requirements for Alberta Infrastructure Facilities”

https://www.alberta.ca/assets/documents/infra-technical-design-requirements.pdf

All documents can be found on Infrastructure’s Technical Resource Centre, Guidelines and Standards page:  https://www.alberta.ca/guidelines-and-standards-owned-and-supported.aspx

1.	General

SUMMARY

This section includes requirements for the supply and install of modular carpet with all necessary trims and accessories required for a complete installation.

1.1	RELATED Requirements

| .1 | Ceramic Tile Flooring | Section 09 30 00 |
| --- | --- | --- |
| .2 | Resilient Flooring | Section 09 65 00 |
| .3 | Access Flooring | Section 09 69 00 |
| .4 | Room Finish Schedule | Section 09 99 99 |
| .5 | Concrete Floor Finishing | Section 03 35 00 |

SPEC NOTE:  Normally specify carpet removal in Division 02, if other demolition work is also required.  If carpet removal will be the only demolition work, specify it in this Section.

  - REFERENCE STANDARDS

| .1 |  | ASTM International (ASTM): |
| --- | --- | --- |
|  | .1 | ASTM E648 Class 1 (glue down) – Standard test method for critical radiant flux of floor-covering systems using a radiant heat Energy Source; |
|  | .2 | ASTM E662 – 21ae1– Standard test method for Specific optical density of smoke generated by solid materials; |
|  | .3 | ASTM D5252-20 – Standard practice for the operation of the Hexapod Tumble Drum Tester; |
|  | .4 | ASTM F710-21, Standard Practice for Preparing Concrete Floors to Receive Resilient Flooring; |
|  | .5 | ASTM F1869-16a, Standard Test Method for Measuring Moisture Vapor Emission Rate of Concrete Subfloor Using Anhydrous Calcium Chloride; |
|  | .6 | ASTM- F2170-19a, Standard Test Method for Determining Relative Humidity in Concrete Floor Slabs Using in situ Probes. |

| .2 | Carpet and Rug Institute (CRI): |
| --- | --- |
|  | .1 | CRI 104-2015, Standard for Installation of Commercial Carpet; |
|  | .2 | CRI Indoor Air Quality Carpet Testing Program. |
| .3 | American Association of Textile Chemists and Colorists: |
|  | .1 | Color Fastness to Lightfastness AATCC TM16-2014e2; |

| .4 | American Association of Textile Chemists and Colorists (AATCC): |
| --- | --- |
|  | .1 | Electrostatic Propensity of Carpet, AATCC TM134-2019 under 3.5KV; |

| .5 | Underwriters’ Laboratories of Canada (ULC): |
| --- | --- |
|  | .1 | CAN/ULC-S102.2:2018, Surface Burning Characteristics of Building Materials and Assemblies; |

1.3	PRODUCT OPTIONS AND SUBSTITUTIONS

| .1 | Refer to Division 01 for requirements pertaining to Section 01 62 00 Product Options and Substitutions. |
| --- | --- |

SPEC NOTE: DELETE IF NOT A LEED PROJECT

1.4	Leed REquirements

.1	Coordinate with Section 01 35 18 – LEED Requirements.

1.5	SUBMITTALS (Tile LAYOUT DRAWINGS AND SAMPLES)

| .1 | Comply with submittal requirements of Division 01, Section 01 33 23 Shop Drawings, Product Data and Samples, Section 01 33 00 Submittal Procedures. |
| --- | --- |

| .2 | Submit two sets of carpet module layout drawings, complete with modular carpet schedule and room designation consistent with construction drawings. |
| --- | --- |

| .3 | Submit two complete sets of modular carpet manufacturer's running line range. Ensure each set is labeled with the following: |
| --- | --- |
|  | .1 | Manufacturer’s name |
|  | .2 | Pattern (Collection Series) |
|  | .3 | Color |
|  | .4 | Fiber |
|  | .5 | Dye method |
|  | .6 | Oz. weight |
|  | .7 | Manufacturers Installation Options |

| .4 | Upon selection of colour and pattern, submit two full size modular carpet samples in selected color and pattern. |
| --- | --- |

| .5 | Submit maintenance data in accordance with Division 01, Section 01 78 23 Operation and Maintenance Data Manuals. |
| --- | --- |

| .6 | Visit site to inspect for special procedures and perimeter conditions. |
| --- | --- |

1.6	MAINTENANCE MATERIALS

| .1 | Submit and comply with requirements in accordance with Division 01, Section 01 78 43 Spare Parts and Maintenance Materials. |
| --- | --- |

| .2 | Prior to installation, provide extra materials as described below. Extra materials to be packaged with protective covering for storage. Identify extra materials with labels describing contents. |
| --- | --- |

| .3 | Extra Stock: Provide full size units equal to [5-7] [ ] percent of each type, colour and pattern required. [Store on site as directed] [ ] . |
| --- | --- |

| .4 | Maintenance materials to be from the same product run as installation materials. |
| --- | --- |

1.7	ENVIRONMENTAL REQUIREMENTS (CONDITIONS)

| .1 | Maintain minimum temperature of 18°C in installation areas for a minimum of 48 hours prior to, during and 48 hours after installation. |
| --- | --- |

| .2 | Operate ventilation fans of appropriate size, at maximum capacity during modular carpet and adhesive removal and during and for at least 72 hours after glue-down installation. |
| --- | --- |

1.8	REMOVAL OF EXISTING CARPET, ADHESIVE AND WASTE REMOVAL

SPEC NOTE:  Include this article when existing carpet is being removed and not part of selective demolition specified in Division 02.

| .1 | Separate and recycle waste management and disposal in accordance with Section 01 74 19 Waste Management and Disposal. |
| --- | --- |

| .2 | Refer to Division 01 for requirements pertaining to noise and dust control and use of premises. |
| --- | --- |

| .3 | Use vacuum equipped with power head/sweeper to vacuum existing carpet prior to removal. |
| --- | --- |

| .4 | Apply fine mist water spray to carpet to minimize dust generation during removal. Avoid spraying near electrical outlets. |
| --- | --- |

| .5 | Remove from site existing carpet as indicated. |
| --- | --- |

| .6 | Remove and salvage existing modular carpet as indicated. |
| --- | --- |

| .7 | [Salvaged materials shall remain property of the Province]. Salvaged materials [to remain on site as directed by the Province] [ ]. |
| --- | --- |

| .8 | Vacuum floor after existing modular carpet has been removed. |
| --- | --- |

| .9 | Remove existing carpet accessories [and [ ]] [and wall base] from areas indicated to receive new flooring materials. |
| --- | --- |
| .10 | Inspect substrate for smooth finish. [Remove adhesive remaining on substrate]. [Remove trowel tracks and rough remaining adhesive using mechanical means]. |

SPEC NOTE:  Include .11  if applicable.

| [.11 | Retain [ ] for re-installation as indicated.] |
| --- | --- |

1.9	PRODUCT HANDLING, DELIVERY AND STORAGE

| .1 | Deliver modular carpet and other accessories in original cartons or packaging clearly marked with the manufacturer’s name, material description, colour, pattern, size, type, dye lot and quantity. |
| --- | --- |

| .2 | Store under cover and away from moisture. Keep dry at all times. |
| --- | --- |

SPEC NOTE:  Include if applicable.

| [.3 | Deliver modular carpet to and store at the following location during performance of the Work]: |
| --- | --- |

|  | [ ] |  |
| --- | --- | --- |

|  | .1 | Coordinate delivery with the Province. |
| --- | --- | --- |
|  | [ ] |  |

| .4 | Deliver modular carpet from the [ ] to the [ ] in portions, as required, to perform the Work. |
| --- | --- |

|  | .1 | Coordinate delivery with the Province. |
| --- | --- | --- |

| .5 | Extra stock will be stored in the [ ] as directed by the Province. |
| --- | --- |

1.10		WARRANTY

| .1 | Manufacturer Warranty: |
| --- | --- |
|  | .1 Provide manufacturers warranty for 10 years from date of Substantial Performance and as follows: .1 10 year limited abrasive wear warranty. .2 Lifetime limited anti-static warranty. .3 Lifetime limited no zipper or edge ravel warranty. |

1.11		PROJECT CONDITIONS

| .1 | Do not install modular carpet until wet work in spaces is complete and dry and that ambient temperature and humidity conditions are maintained at the levels when space will be occupied for its intended use. |
| --- | --- |

| .2 | Do not install modular carpet over concrete subfloor until slabs have cured and are sufficiently dry to bond with adhesive and concrete subfloor have pH range recommended by carpet manufacturer. |
| --- | --- |

| [.3 | [Moisture content not to exceed 75% rh test method as per ASTM F2170]. |
| --- | --- |

| [.4 | [Pre-installation moisture and alkalinity test as per ASTM test standards]. |
| --- | --- |

| .5 | Comply with CRI 104, Site Conditions: Temperature and Humidity. |
| --- | --- |

1.12		COORDINATION

SPEC NOTE:  Edit or delete this article to suit project requirements.

| .1 | Install modular carpet prior to installation of: |
| --- | --- |
|  | .1 | [ Partitions ]. |
|  | .2 | [ Moveable partitions]. |
|  | .3 | [ Furniture]. |
|  | .4 | [ Telephone and electrical power pedestal outlets]. |
|  | .5 | [ Covered resilient base]. |
|  | .6 | [ Wood bases]. |

| .2 | Install modular carpet after the installation of: |
| --- | --- |
|  | .1 | [ ]. |
|  | .2 | [ ]. |

2.	Products

2.1	material Components

| .1 | Modular carpet construction must meet or exceed the following: |
| --- | --- |
|  | .1 | Fibre Content: 100% nylon, bulk continuous filament, and permanently conductive fibres to control electrostatic propensity. |
|  | .2 | Dye Method: 90% Solution Dyed, 10% Space Dyed minimum. |
|  | .3 | Pile Characteristics: Multi-level loop, textured level loop, or level loop. |
|  | .4 | Tufted Weight: 18 oz. minimum. |
|  | .5 | Gauge: 1/10” minimum. |
|  | .6 | Stitches per inch: 8.00” minimum. |
|  | .7 | Pile Density: 6000oz./cy minimum. |
|  | .8 | Modular unit size: [ ]. |
|  | .9 | Shape: Rectilinear (square or rectangular). |
|  | .10 | Backing System: |
|  |  | .1 | Manufacturers standard vinyl or thermoplastic hard backed or cushion thermoplastic or pvc-free open cell urethane cushion backing system. |
|  |  | .2 | Recyclable content. |
|  |  | .3 | Maintaining a 100% true moisture barrier between the secondary backing and the substrate below. |
|  |  | [.4 | A pre-adhered backing system may be used as an alternate to an applied releasable adhesive to the surface substrate.] |
|  | .11 .12 .13 .14 .15 | Color and Pattern: Province to select from manufacturers standard color range. Modular carpet to be a [non-direction] [quarter turn] [random] [monolithic] [ashlar] [brick] [ ] pattern. Inherent Static Control less than 3.5 Kilovolts at 21°C and 20% relative humidity. Delimitation to ASTM D3936 to min 2.5 Lbs/in. Soil/Stain protection. |

2.2	ACCESSORIES

SPEC NOTE:  Retain only clauses applicable to the installation.

| .1 | Cementitious Underlayment: [self-leveling and trowel grade ], [ pre-mixed ], [ polymer-modified], containing no gypsum, not softened by water after final set. Minimum compressive strength 10 MPa at 24 hours and 20 Mpa at 7 days. Suitable for floor covering installation not more than 12 or 4 hours after application. |
| --- | --- |
| .2 | Releasable pressure sensitive type adhesive: [adhesive must be water-based and allow for removal of modular carpet at any time without damager to carpet ] or [ substrate adhesive must contain antimicrobial preservative ] and have “zero” calculated Volatile Organic Compounds (VOCs). |

| .3 | Modular Carpet Edge Guard: as follows: |
| --- | --- |
|  | .1 | Type: non-metallic, extruded or molded heavy-duty rubber "T" shaped cap insert and minimum 50 mm wide extruded aluminum anchorage flange, profiled to accept cap. |
|  | .2 | Colour: selected from manufacturer's standard range. [A different colour will be selected for each different colour of modular carpet]. |

| .4 | Carpet Stair Nosings: [vinyl] [rubber], [double] [single] butt, square nose, 10 mm thick, 8 mm butting gauge, 25 mm vertical face [and 25 mm vertical lip, 40 mm horizontal face and 45 mm horizontal lip, [one-piece length for stair nosing] [[2.74][3.66] m lengths], [standard] colour [indicated in schedule]. |
| --- | --- |

SPEC NOTE:  Delete stair nosings if not applicable or if specified in Section 09 65 00. Installing carpet on stairs, without nosings, is not recommended.

SPEC NOTE: Specify rubber nosings for heavy traffic.  Specify double butt stair nosings when both treads and risers are carpeted, single butt if carpet only on treads.  Delete vertical lip if single butt specified.  Rubber comes in 2.74 m lengths; vinyl in 3.66 m.

| .5 | Modular Carpet Base Cap Strip: purpose made, extruded [vinyl] [metal] cap strip to accommodate carpet base thickness [and wrap over top edge of base], colour [to match carpet] [to be from manufacturer’s full colour range]. |
| --- | --- |

SPEC NOTE:  Specify carpet base cap strip only when carpet base is specified and binding of exposed edge of carpet base is not specified.

2.3	RESILIENT BASE

SPEC NOTE:  Include this article if applicable in conjunction with carpet.

| .1 | Resilient Base: to ASTM F1861-16 and as follows: |
| --- | --- |
|  | .1 | Type: TP, rubber, thermoplastic. |
|  | .2 | Group: 1, solid. |
|  | .3 | Style: [cove] [toeless]. |
|  | .4 | Thickness: 3.2 mm. |
|  | .5 | Height: [63.5] [101.6] [152.4] mm. |
|  | .6 | End Stops and External Corners: pre-molded. |
|  | .7 | Colour: [standard] colour [indicated in schedule]. A different colour will be selected for each type of carpet specified. |
| .2 | Re-install resilient base, measuring 1 meter or longer in length, removed for modular carpet installation. |

| .3 | Supply and install new [rubber] base to replace damaged and missing [PVC or rubber] base, as applicable. Utilize building standard. |
| --- | --- |

3.	Execution

3.1		EXAMINATION (CONDITION OF SUBSTRATE)

| .1 | Examine substrates, areas, and conditions, for compliance with requirements for maximum moisture content, alkalinity range, installation tolerance and other conditions that may affect the performance of the modular carpet. |
| --- | --- |

3.2	PREPARATION

SPEC NOTE:  Leveling Include this article only where entire areas need to be re-surfaced by the flooring installer, using a self-levelling underlayment.  Unusually large deviations in concrete floors may require grinding or the use of concrete toppings. Involve the services of a professional engineer before specifying concrete topping in Division 03.

| .1 | Comply with CRI 104, Site conditions: Floor Preparation and Carpet Manufacturers written installation instructions for preparing substrates indicated to receive modular carpet installation. |
| --- | --- |

| .2 | Use trowelable leveling and patching compounds, according to manufacturer’s written instructions, to fill cracks, holes, depressions and protrusions in the substrate. Fill or level cracks, holes and depressions 3mm wide or wider and protrusions more than 0.8mm, unless more stringent requirements are identified in the carpet manufacturer’s written instructions. |
| --- | --- |

| .3 | Trowel and float to produce a smooth, flat surface. Allow to cure properly. |
| --- | --- |

| .4 | Remove coatings, including curing compounds and other substances from concrete subfloor that are not compatible with adhesives and that contain soap, wax, oil, or silicone, without using solvents using mechanical methods recommended in writing by the carpet manufacturer. |
| --- | --- |

| .5 | Broom and vacuum clean substrate to remove dust and other small particles. Cover prior to installing modular carpet. |
| --- | --- |

| .6 | Substrate to have acceptable level of absorbency as per manufacturer’s written instructions. After cleaning, examine substrates for acceptable levels of moisture, alkaline salts, carbonation, or dust before proceeding with installation. |
| --- | --- |
| .7 | When underlayment has cured, clean substrate surface and allow to dry. |

| .8 | To ensure requirements are achieved test cementitious substrate for porosity, moisture content and alkalinity. |
| --- | --- |

  - INSTALLATION

| .1 | Install modular carpet using a minimum number of pieces of carpet modules. |
| --- | --- |

| .2 | Comply with CRI 104, Section 10, “Carpet Tile,” and with carpet manufacturer’s written installation instructions. |
| --- | --- |

| .3 | [Comply with CRI 104, Section 8, direct Glue-Down Installation or as per carpet manufacturers written instructions; install every carpet module with full spread, releasable, pressure sensitive adhesive as per manufacturers written instructions] or [Install using releasable, pressure sensitive dry adhesive [tabs] [connectors] [ ] applied to the underside of each module to [float] [adhere] the carpet modules on a clean and level prepared floor. Follow carpet manufacturer’s instructions.] |
| --- | --- |

| .4 | Ensure product and substrate temperature is 18 degrees Celsius minimum where direct glue-down installation is used. Adhesives to be applied in accordance with manufacturers written instructions and adhesive readiness should be verified before beginning installation. |
| --- | --- |

| .5 | Install modular carpet pattern parallel to walls and boarders and as indicated in [Finish Schedule ] [ ]. |
| --- | --- |

| .6 | Install modular carpet smooth and free of bubbles, puckers and defect. Confirm modular carpet type, color and pattern prior to installation. Carpet that is of the same style/color, but from different dye lots and/or manufacturing dates, may be merged and used interchangeably, both at initial installation and at later selective replacement, to create a continuous carpeted surface with no module appearing out of place. |
| --- | --- |

| .7 | Carpet module cuts to be a “clean cut”. Fit modular carpet tight to intersection with vertical surfaces without gaps. |
| --- | --- |

| .8 | All edge transition strips to be installed completely, conceal all exposed edges. |
| --- | --- |

| .9 | Do not bridge building expansion joints with modular carpet. |
| --- | --- |

| [.10 | Install seams in accordance with carpet manufacturer’s written instructions for seam locations] and [direction of carpet modules ]. |
| --- | --- |

| .11 | Cut and fit carpet modules to butt tightly to vertical surfaces, permanent fixtures, and built-in furniture including cabinets, pipes, outlets, edgings, thresholds, and nosings. |
| --- | --- |

| .12 | Bind or seal cut edges as per carpet manufacturer’s written instructions. |
| --- | --- |

| .13 | Extend carpet modules into toe spaces, door reveals, closets, open-bottomed obstructions, removable flanges, alcoves, and similar openings. |
| --- | --- |
| .14 | Maintain all reference markers, openings and holes that are in place or marked for future cutting. |

| .15 | Roll carpet for complete contact of carpet modules with adhesive and substrate. |
| --- | --- |

3.4	INSTALLATION AT OUTLET BOXES/FLOOR ACCESS PANELS

| .1 | Locate and cut carpet modules to fit over access panels. |
| --- | --- |

| .2 | Fully adhere carpet modules to panels and adjacent subfloor. |
| --- | --- |

3.5	INSTALLATION OF RESILIENT BASE

SPEC NOTE:  Include this article if applicable in conjunction with carpet.

| .1 | Install resilient base in accordance with Section 09 65 00 Resilient Base. |
| --- | --- |

| .2 | Fit joints tight and vertical. |
| --- | --- |

| .3 | [Mitre internal corners ]. [Use pre-molded sections for external corners and exposed ends ]. |
| --- | --- |

| .4 | Install base on solid backing. Adhere tightly to wall and floor surfaces. |
| --- | --- |

| .5 | Scribe and fit to door, frames and other obstructions. |
| --- | --- |

| .6 | Install straight and level to variation of plus or minus 3 mm over 3 m straight edge. |
| --- | --- |

3.6	CLEANING and protection

| .1 | Use protection and cleaning procedures and / or methods as per manufacturers written instructions. |
| --- | --- |

| .2 | After installing modular carpet: |
| --- | --- |
|  | .1 | Remove excess adhesive, seam sealer and other surface blemishes using cleaner recommended by carpet manufacturer written instructions. |
|  | .2 | Remove yarns that protrude from modular carpet surface. |
|  | .3 | Vacuum modular carpet. |

| .3 | Protect installed modular carpet from damage and soiling from construction operations and placement of equipment and fixtures during the remainder of the construction period. |
| --- | --- |

3.7	TRAINING

| .1 | Provide (a) qualified representative(s) from the carpet manufacturer to instruct building maintenance staff in proper methods for installing, maintaining modular carpet, including environmental friendly cleaning and stain removal products and procedures as per manufacturer’s written maintenance review. |
| --- | --- |

END OF SECTION