Section Cover Page

Section 09 72 16 2014-11-01 Vinyl Coated Fabric Wall Coverings

Refer to “LEED Notes and Credits” page for additional guidance for LEED projects. Delete LEED items if project: .1 is excluded by the Department’s policy on LEED, or .2 the Department has determined that the work of this Contract is not to attain a LEED rating.

This Master Specification Section contains:

.1	This Cover Sheet

.2	LEED Notes and Credits

.3	Specification Section Text:

1.	General

1.1	Related Work Specified in Other Sections

1.2	Reference Documents

1.3	Submittals

1.4	Maintenance Material Submittals

1.5	Quality Assurance

1.6	Delivery, Storage, and Handling

1.7	Site Condition

2.	Products

2.1	Materials

3.	Execution

  - Conditions of Surfaces

  - Preparation

3.3	Application

3.4	Cleaning

3.5	Wall Fabric Schedule

LEED Notes:

If the project is not a designated LEED project, but is following sustainable building practices, specify that adhesive products meet SCAQMD Rule #1168.

LEED Credits:

Contribution towards LEED credits in this section may apply as follows:

1.	LEED Credit EQ 4.1 Low-Emitting Materials: Sealants and Adhesives. Adhesives specified under this section apply.

In order to obtain EQ 4.1, VOC content in adhesives must be less than the VOC content limits of the State of California’s South Coast Air Quality Management District (SCAQMD) Rule #1168, June 2006. Product data and/or LEED letters from manufacturers are required for verification.

1.	General

1.1	RELATED WORK SPECIFIED IN OTHER SECTIONS

.1	[LEED Submittal Forms	Section 01 32 16.]

.2	[LEED Requirements	Section 01 35 18.]

.3	[Environmental Procedures	Section 01 35 20.]

.4	Waste Management and Disposal	Section 01 74 19.

.5	Painting:	Section [             ].

  - Reference documents

SPEC NOTE: Edit this article to include only standards referenced within the edited version of this Section, including LEED documentation and sustainable practices.

.1	Canada Green Building Council (CaGBC)

| .1 | LEED Canada 2009 Rating System | LEED Canada for New Construction and Major Renovations. LEED Canada for Core and Shell Development. Website: www.cagbc.org.] |
| --- | --- | --- |

.2	Canadian General Standards Board (CGSB)

| .1 | CGSB 41 GP 30M - 82 | Wall Coverings, Vinyl Coated Fabrics |
| --- | --- | --- |

.4	South Coast Air Quality Management District (SCAQMD), California State

| .1 | SCAQMD Rule 1168, June 2006 | Adhesives and Sealants Applications |
| --- | --- | --- |

.5	Underwriters Laboratories of Canada (ULC)

| .1 | CAN/ULC S102-07 | Method of Test for Surface Burning Characteristics of Building Materials and Assemblies. |
| --- | --- | --- |

1.3		submittals

.1	Product Data

.1 	Submit product data, in accordance with Division 01, stating compliance with specified standard.

.2	Submit WHMIS – Material Safety Data Sheets, in accordance with Division 01, for vinyl coated wall fabric and adhesive.

.3	Upon request, submit test data to substantiate that the requirements for Fire Hazard Classifications per Alberta Building Code are met.

.2	Samples

.1	Submit 215 mm x 275 mm samples of wall fabric to the Province for final approval prior to ordering.  Label samples with manufacturer's name, quality, colour, texture and weight.

.3	Sustainable Design Submittals:

SPEC NOTE: Use the following paragraph when LEED Submittals are required:

.1	LEED Submittals: Submit documentation in accordance with Section 01 35 18 – LEED Requirements.  Submit documentation for the following:

.2	Indoor Environmental Quality:

SPEC NOTE: Delete LEED submittal item below if project is not to attain LEED certification or if Credit EQ 4.1 Low Emitting Materials: Adhesives and Sealants is not being sought. If project is to follow sustainable building practices but not attaining LEED certification, delete references to LEED and retain SCAQMD Rule #1168 as a sustainable submittal.

.1	EQ Credit 4.1 - Low-Emitting Materials: Adhesives & Sealants

1.4	maintenance material submittals

SPEC NOTE:  Consider this Article  in relation to project size and use of space.

.1	Extra Stock Materials:

.1	Provide [     ] lineal metres of full width wall fabric material of each pattern and colour.

1.5	quality assurance

.1	Certifications:

.1	Materials shall be approved by Underwriters’ Laboratories of Canada, for Fire Hazard Classifications per Alberta Building Code (ABC) and Alberta Fire Code 2006 editions.

.2	Mock-Ups:

SPEC NOTE:  Include this Article only for large projects or special conditions.

.1	Before proceeding with complete installation, finish one complete surface or item of each colour scheme required showing selected colours, texture, materials and workmanship for approval.

.2	The approved sample surface will be a standard for similar work throughout the building and will remain as part of the finished work.

1.6	DELIVERY, storage, and handling

.1	Delivery and Acceptance Requirements:

.1	Deliver wall fabric material, sealers, and adhesives to site in sealed packages and containers bearing manufacturer's labels and seals.

.2	Storage and Handling Requirements:

.1	Store fabric material flat in a clean, dry storage area where temperature is a minimum 7°C with normal humidity.  Do not store materials in upright position. Protect end of rolled materials from damage.

.2	Store toxic and/or explosive solvents and adhesives in properly ventilated areas.

.3	Take precautionary measures to prevent fire hazards with adhesives and solvents.

.3	Waste Management and Disposal:

.1	Separate waste materials for [reuse] [and] [recycling] in accordance with Section 01 74 19 – Management and Disposal.

1.7	site conditions

.1	Ambient Conditions:

.1	Maintain air temperature, surfaces and materials at minimum 20°C for 72 hours before, during, and 48 hours after application.

.2	Maintain surface moisture to fabric manufacturer's requirements.

2.	Products

  - MATERIALS

SPEC NOTE: Specify texture by description such as: tweed, linen, silk, grass, reed, wood, cork, leather, etc.  If more than one wall fabric is required, repeat and edit paragraph 2.1.1 with properties and renumber Article. Ensure the location of each is clearly specified in schedule or indicated on drawings.

.1	Vinyl covered wall fabric[, Wall Fabric Designation [ ]]: [to meet and exceed CGSB 41-GP-30, 1370 mm finished width, [ULC labeled], [Type 1 - light] [Type 2 - medium] [Type 3 - heavy] duty weight meeting the following minimum requirements:

SPEC NOTE: The following properties are each listed in order of Type from 1 to 3 respectively.

.1	Fabric weight: [68 g/m2], [68 g/m2],  [166 g/m2].

.2	Vinyl weight: [254 g/ m2], [424 g/ m2], [468 g/ m2].

.3	Flame spread: [10], [15], [25].

.4	Fuel contributed: [0], [0], [5].

.5	Smoke developed: [10], [15], [25].

.6	Texture: [              ].

.7	Pattern: [             ]

.2	[Two] colours will be selected, by the Province, for each [texture] [and] [pattern] from wall fabric manufacturer's standard range.

SPEC NOTE:  Delete VOC content requirement below if project is not attaining LEED certification or LEED Credit EQ 4.1 is not being sought, or sustainable building practices are not being followed.

.3	Adhesives: shall be type as recommended by fabric manufacturer to suit application to substrate[and VOC content compliant with SCAQMD Rule #1168, June 2006]. Where permitted as an option by the wall fabric manufacturer, use a water-base adhesive.

3.	Execution

  - CONDITIONS OF SURFACES

SPEC NOTE:  Consult manufacturers for advice if vinyl fabric is to be applied to existing finished surfaces, i.e. painted, etc.

.1	Ensure surfaces to receive wall fabric are clean, true, free of irregularities.

.2	Wall surfaces shall not vary in plane more than 3 mm in any 3 meter dimension or at a rate of line greater than 5 mm per running meter.

.3	Ensure work penetrating substrate is completed before installing wall fabric.

.4	Inspect surfaces and job conditions before commencing work and report defects in writing to the Province.

.5	Prior to application confirm that moisture content of wall does not exceed 6% [confirmed by moisture meter] and that litmus paper test confirms that alkali is not present on or near surface.

.6	Ensure that all surfaces scheduled to receive vinyl coated wall fabric are prime painted with alkyd primer as specified in Section [                   ].

  - Preparation

.1	Protect other surfaces and make good any damage caused by work of this Section.

.2	Remove electrical plates, surface hardware, fittings and fastenings, prior to wall covering operations.  Replace on completion of work in each area.

.3	Prepare substrate surfaces according to wall fabric manufacturer’s recommendations.

.4	Mix adhesive as required to eliminate solids or particles that will telegraph through wall fabric.

3.3	APPLICATION

.1	Apply vinyl coated wall fabric according to manufacturer’s directions.

.2	Follow adhesive manufacturer's directions for mixing and applying adhesive.

.3	Apply adhesive to wall surface using a roller or brush.

.4	Use fabric panels in exact order as cut from rolls; use rolls in consecutive order as numbered by manufacturer.

.5	Trim wall fabric with deeply textured patterns, or patterns that must be matched, on a flat worktable.

.6	Apply wall fabrics with deeply textured patterns, or patterns that must be matched, by pasting strips on the wall with patterns matching and with edges tight, eliminating both overlapped and open seams.

.7	Apply wall fabrics with smooth, non-match patterns by pasting strips on the wall, overlapping the edges and "double cutting" through both layers.

.8	Seams shall be plumb and true to line.

.9	Eliminate air pockets and ensure full bond of the wall covering to the wall surface.

.10	Apply to areas above and below windows, above doors and similar areas in sequence from the roll.

.11	Remove excess adhesive from each seam before proceeding to next seam.  Wipe seam clean with dry cloth towel.

.12	Install fabric secure, smooth, clean, without wrinkles, gaps or overlaps.

.13	Horizontal seams will not be accepted.  Cutting at corners will not be accepted.  Cutting for corners shall be within 50 mm of an inside corner and within 150 mm of an outside corner.

.14	Ventilation:

.1	Provide adequate and continuous ventilation during work and for 24 hours after installation of wall fabric.

3.4	CLEANING

.1	Clean wall coverings and adjacent surfaces of adhesives, dust, dirt and other contaminates.

.2	Use cleaner that will not remove or disfigure adjacent finishes.

.3	Remove debris and leave areas neat and clean.

  - wall fabric schedule

SPEC NOTE: Use this schedule if wall fabric location and description is not indicated on drawings.

Edit to suit project requirements.

| Wall Fabric Designation | Location |
| --- | --- |
|  | Rooms | Walls | Height |
| No. 1 | [101], [103], [105] | [North] | [Full] |
| No. 2 | [102], [104], [106] | [South] | [Full] |
| No. 3 | [Boardrooms] | [All] | [900 mm height] |
| No. 4 | [Boardrooms] | [All] | [900 mm to ceiling,2750 mm ] |

END OF SECTION