Section Cover Page

Section 09 91 15 Exterior Repainting and 2014-11-01 Refinishing Schedule

Refer to “LEED Notes and Credits” page for additional guidance for LEED projects. Delete LEED items if project: .1 is excluded by the Department’s policy on LEED, or .2 the Department has determined that the work of this Contract is not to attain a LEED rating.

Use this Section to schedule finishing systems for all previously finished, exterior substrates requiring site repainting or refinishing.

The Infrastructure, Basic Master Specification contains the following series of Sections that specify site painting and finishing:

.1	Section 09 91 05 - Painting and Finishing General Requirements

.2	Section 09 91 13 - Exterior Painting and Finishing Schedule

.3	Section 09 91 15 - Exterior Repainting and Refinishing Schedule (this Section)

.4	Section 09 91 23 - Interior Painting and Finishing Schedule

.5	Section 09 91 25 - Interior Repainting and Refinishing Schedule

.6	Section 09 91 30 - Painting of Mechanical and Electrical Work

These sections are interrelated.  Section 09 91 05 specifies general requirements while the remaining Sections in the series specify finish systems, i.e. specific products and number of coats, required for various types of substrates.  Always include Section 09 91 05.  Include one or more of the remaining Sections only to the extent they are applicable to the project.

This Master Specification Section contains:

.1	This Cover Sheet

.2	LEED Notes and Credits

.3	Data Sheet - General

.4	Specification Section Text:

1.	General

1.1	Intent

2.	Products

(Not used)

3.	Execution

3.1	Exterior Repainting and Refinishing Schedule

LEED Notes:

LEED does not require paints and coatings applied to the exterior of the building to have low VOC content. The EQ credit is for Indoor Air Quality only.

However, sustainable building practices could be applied to exterior coatings as well. If this is done it is better to follow MPI Green Performance Standards GPS-01 and GPS-02 to ensure that the product has adequate performance as well as lower VOC content.

LEED Credits:

N/A

This Section includes a comprehensive listing of previously finished, exterior, substrates, complete with MPI code numbers, finishing system descriptions and product descriptions.

Individual finishing systems listed in this master schedule must be edited to suit the project. Note that the schedule generally calls for repainting and refinishing with 2 coats, after priming to suit the degree of deterioration.  Two coats are recommended if a high quality result is desired.  If repainting/refinishing with a single coat is deemed adequate, or if project budget does not permit two coats, the schedule must be edited accordingly.

Specifier has the option of scheduling site repainting and refinishing by one of two methods:

.1	Method #1:  Indicate on drawings, on exterior finish schedule, or elsewhere as appropriate, the proper code designation and where applicable, gloss level, of the required finish system for each item or substrate that requires site repainting or refinishing.  In this Section, specify the finish system corresponding to each required finish.  Coordinate with drawings, exterior finish schedule, etc.

.2	Method #2:  Incorporate a comprehensive listing of each item or substrate that requires site repainting or refinishing into this Section.  Do not indicate code designations elsewhere.  Since this Section describes substrate elements in general terms only, mainly for reference purposes, it may require modification and expansion to include more specific and detailed substrate descriptions.  Use this method only where exterior repainting and refinishing are minimal.

Carefully consider all surfaces to be repainted or refinished and ensure that appropriate finishing systems are specified for each surface type. Review the system evaluation and surface preparation sections of the MPI Maintenance Repainting Manual when selecting finishing systems.

Specify only those finishing systems that are applicable to the project.  Delete all other finishing systems.

END OF DATA SHEET

1.	General

1.1	INTENT

.1	Read this Section in conjunction with Section 09 91 05 - Painting and Finishing General Requirements.

2.	Products

.1	(Not used).

3.	Execution

3.1	extERIOR PAINTING AND FINISHING SCHEDULE

.1	The following systems with codes numbers, finishing system description, gloss levels, coats and product descriptions are derived from the MPI Maintenance Repainting Manual and the MPI Approved Products List.

.2	Prime substrate, referencing the 1st coat, for the Degree of Surface Deterioration codes as recommended by the MPI Maintenance Repainting Manual and as follows:

.1	DSD 1:  Touch-up.

.2	DSD 2:  Spot prime.

.3	DSD 3:  Full prime coat.

.3	Where the finishing system requires different product for first coats, DSD 1, 2 or 3, the MPI product numbers will be noted in the finishing system description.

SPEC NOTE: Determine the required priming and ensure the appropriate DSD is specified for each applicable finishing system.

SPEC NOTE: Delete finishing systems as required to include only systems required for the project. Edit all option fields.  Where more than one Gloss Level is required for a particular substrate, include all applicable gloss levels and ensure location of various gloss levels are clearly defined in Section 09 91 05, Article 2.4, Paragraph 2.4.2

# REX 2.1 – ASPHALT SURFACES

| REX 2.1A | Latex Zone / Traffic Marking | Latex Zone/Traffic Marking Paint, Apply in strict accordance with manufacturer’s instructions. |
| --- | --- | --- |
| REX 2.1B | Alkyd Zone / Traffic Marking | Alkyd Zone/Traffic Marking Paint, Apply in strict accordance with manufacturer’s instructions. |

REX 3.1 – CONCRETE VERTICAL SURFACES

| REX 3.1A | Latex | 1st | DSD [1] [2] [3] |
| --- | --- | --- | --- |
|  | Gloss level [G1] [G5] [G6] | 2nd | Latex |
|  |  | 3rd | Latex |
| REX 3.1B | Latex Aggregate | Latex Aggregate, Apply in strict accordance with manufacturer’s instructions. |
|  | [Coarse] [Medium] texture, |  |
|  | Gloss level [G1] [G5] [G6] |  |
| REX 3.1C | Waterborne Light Industrial Coating | 1st | DSD [1] [2] [3] |
|  | Gloss level [G3] [G5] [G6] | 2nd | W. B. Light Industrial Coating |
|  |  | 3rd | W. B. Light Industrial Coating |
| REX 3.1D | Epoxy | 1st | DSD [1] [2] [3] |
|  |  | 2nd | Epoxy |
|  |  | 3rd | Epoxy |
| REX 3.1E | Epoxy, Water Based | 1st | DSD [1] [2] [3] |
|  |  | 2nd | W. B. Epoxy |
|  |  | 3rd | W. B. Epoxy |
| REX 3.1F | Elastomeric | Elastomeric Coating, Apply in strict accordance with manufacturer’s instructions. |
| REX 3.1G | Water Repellent | Water Repellent, Apply in strict accordance with manufacturer’s instructions. |
|  | (not paintable) |  |
| REX 3.1H | Water Repellent | Water Repellent, Apply in strict accordance with manufacturer’s instructions. |
|  | (paintable) |  |
| REX 3.1J | High Build Latex | High Build Latex, Apply in strict accordance with manufacturer’s instructions. |
| REX 3.1K | Concrete Stain | Concrete Stain, Apply in strict accordance with manufacturer’s instructions. |
| REX 3.1L | Latex | 1st | DSD [1] [2] [3] |
|  | Gloss level [G1] [G5] [G6] | 2nd | Latex |
|  | (DSD 2 or 3 – MPI # 3) | 3rd | Latex |
| REX 3.1M | Polyurethane, Pigmented | 1st | DSD [1] [2] [3] |
|  | (DSD 2 or 3 – MPI # 77) | 2nd | Polyurethane |
|  |  | 3rd | Polyurethane |

REX 3.2 – CONCRETE HORIZONTAL SURFACES

| REX 3.2A | Latex Floor Paint | 1st | DSD [1] [2] [3] |
| --- | --- | --- | --- |
|  | Gloss level [G3] [G6] | 2nd | Floor Paint |
|  |  | 3rd | Floor Paint |
| REX 3.2B | Latex Deck Coating | Latex, Apply in strict accordance with manufacturer’s instructions. |
| REX 3.2C | Epoxy Non-slip Deck Coating | Epoxy, Apply in strict accordance with manufacturer’s instructions. |
| REX 3.2D | Alkyd Floor Enamel | 1st | DSD [1] [2] [3] |
|  | Gloss level [G4] [G6] | 2nd | Alkyd |
|  |  | 3rd | Alkyd |
| REX 3.2E | Latex Zone / Traffic Marking | Latex, Apply in strict accordance with manufacturer’s instructions. |
| REX 3.2F | Alkyd Zone / Traffic Marking | Alkyd, Apply in strict accordance with manufacturer’s instructions. |
| REX 3.2G | Sealer, Clear | 1st | DSD [1] [2] [3] |
|  |  | 2nd | Clear Sealer |
|  |  | 3rd | Clear Sealer |
| REX 3.2H | Sealer, Clear, Water Based | 1st | DSD [1] [2] [3] |
|  |  | 2nd | Clear Sealer |
|  |  | 3rd | Clear Sealer |
| REX 3.2J | Concrete Stain | Concrete Stain, Apply in strict accordance with manufacturer’s instructions. |

REX 3.3 – CEMENTITIOUS COMPOSITION BOARD

| REX 3.3A | Latex | 1st | DSD [1] [2] [3] |
| --- | --- | --- | --- |
|  | Gloss level [G1] [G5] [G6] | 2nd | Latex |
|  |  | 3rd | Latex |
| REX 3.3B | Alkyd | 1st | DSD [1] [2] [3] |
|  | Gloss level [G1] [G5] [G6] | 2nd | Alkyd |
|  | (DSD 2 or 3 – MPI # 6) | 3rd | Alkyd |
| REX 3.3C | Waterborne Light Industrial Coating | 1st | DSD [1] [2] [3] |
|  | Gloss level [G3] [G5] [G6] | 2nd | W. B. Light Industrial Coating |
|  |  | 3rd | W. B. Light Industrial Coating |
| REX 3.3D | Epoxy, Water Based | 1st | DSD [1] [2] [3] |
|  |  | 2nd | W. B. Epoxy |
|  |  | 3rd | W. B. Epoxy |
| REX 3.3E | Epoxy | 1st | DSD [1] [2] [3] |
|  |  | 2nd | Epoxy |
|  |  | 3rd | Epoxy |
| REX 3.3F | Polyurethane, Pigmented | 1st | DSD [1] [2] [3] |
|  | (DSD 2 or 3 – MPI # 77) | 2nd | Polyurethane |
|  |  | 3rd | Polyurethane |
| REX 3.3G | Latex Aggregate | Latex Aggregate, Apply in strict accordance with manufacturer’s instructions. |
|  | [Coarse] [Medium] texture |  |
|  | Gloss level [G1] [G5] [G6] |  |
| REX 3.3H | High Build Latex | High Build Latex, Apply in strict accordance with manufacturer’s instructions. |
| REX 3.3J | Latex | 1st | DSD [1] [2] [3] |
|  | (over alkali resistant primer) | 2nd | Latex |
|  | Gloss level [G1] [G5] [G6] | 3rd | Latex |
|  | (DSD 2 or 3 – MPI # 3) |  |  |

REX 4.1 – CLAY MASONRY UNITS

| REX 4.1A | Latex | 1st | DSD [1] [2] [3] |
| --- | --- | --- | --- |
|  | Gloss level [G1] [G5] [G6] | 2nd | Latex |
|  | (DSD 2 or 3 – MPI # 10) | 3rd | Latex |
| REX 4.1B | Latex Aggregate, [Coarse] [Medium] texture, Gloss level [G1] [G5] [G6] | Latex Aggregate, Apply in strict accordance with manufacturer’s instructions. |
| REX 4.1C | Waterborne Light Industrial Coating | 1st | DSD [1] [2] [3] |
|  | Gloss level [G3] [G5] [G6] | 2nd | W. B. Light Industrial Coating |
|  |  | 3rd | W. B. Light Industrial Coating |
| REX 4.1D | Epoxy | 1st | DSD [1] [2] [3] |
|  | (for smooth brick) | 2nd | Epoxy |
|  |  | 3rd | Epoxy |
| REX 4.1E | Epoxy, Water Based | 1st | DSD [1] [2] [3] |
|  | (for smooth brick) | 2nd | W. B. Epoxy |
|  |  | 3rd | W. B. Epoxy |
| REX 4.1F | Water Repellent | Water Repellent, Apply in strict accordance with manufacturer’s instructions |
|  | (not paintable) |  |
| REX 4.1G | Water Repellent | Water Repellent, Apply in strict accordance with manufacturer’s instructions |
|  | (paintable) |  |
| REX 4.1H | High Build Latex | High Build Latex, Apply in strict accordance with manufacturer’s instructions. |
| REX 4.1J | Polyurethane, Pigmented | 1st | DSD [1] [2] [3] |
|  | (DSD 2 or 3 – MPI # 77) | 2nd | Polyurethane |
|  |  | 3rd | Polyurethane |

REX 4.2 – CONCRETE MASONRY UNITS

| REX 4.2A | Latex | 1st | DSD [1] [2] [3] |
| --- | --- | --- | --- |
|  | Gloss level [G1] [G5] [G6] | 2nd | Latex |
|  |  | 3rd | Latex |
| REX 4.2B | Latex Aggregate | Latex Aggregate, Apply in strict accordance with manufacturer’s instructions. |
|  | [Coarse] [Medium] texture |  |
|  | Gloss level [G1] [G5] [G6] |  |
| REX 4.2C | Waterborne Light Industrial Coating | 1st | DSD [1] [2] [3] |
|  | Gloss level [G3] [G5] [G6] | 2nd | W.B. Light Industrial Coating |
|  |  | 3rd | W.B. Light Industrial Coating |
| REX 4.2D | Elastomeric | Elastomeric Coating, Apply in strict accordance with manufacturer’s instructions. |
| REX 4.2E | Epoxy | 1st | DSD [1] [2] [3] |
|  |  | 2nd | Epoxy |
|  |  | 3rd | Epoxy |
| REX 4.2F | Epoxy, Water Based | 1st | DSD [1] [2] [3] |
|  |  | 2nd | W. B. Epoxy |
|  |  | 3rd | W. B. Epoxy |
| REX 4.2G | Polyurethane, Pigmented | 1st | DSD [1] [2] [3] |
|  | (DSD 2 or 3 – MPI # [98] [108]) | 2nd | Polyurethane |
|  |  | 3rd | Polyurethane |
| REX 4.2H | Water Repellent | Water Repellent, Apply in strict accordance with manufacturer’s instructions. |
|  | (not paintable) |  |
| REX 4.2J | Water Repellent | Water Repellent, Apply in strict accordance with manufacturer’s instructions. |
|  | (paintable) |  |
| REX 4.1K | High Build Latex | High Build Latex, Apply in strict accordance with manufacturer’s instructions. |
| REX 4.2L | Latex | 1st | DSD [1] [2] [3] |
|  | Gloss level [G1] [G5] [G6] | 2nd | Latex |
|  | (DSD 2 or 3 – MPI # 3) | 3rd | Latex |

REX 5.1 – STRUCTURAL STEEL & METAL FABRICATIONS

| REX 5.1A | Quick Dry Enamel | 1st | DSD [1] [2] [3] |
| --- | --- | --- | --- |
|  | Gloss level [G5] [G6] | 2nd | Quick Dry Enamel |
|  | (DSD 2 or 3 – MPI # [76] [95]) | 3rd | Quick Dry Enamel |
| REX 5.1B | Waterborne Light Industrial Coating | 1st | DSD [1] [2] [3] |
|  | (over zinc rich primer) | 2nd | W.B. Light Industrial Coating |
|  | Gloss Level [G3] [G5] [G6] | 3rd | W.B. Light Industrial Coating |
|  | (DSD 2 or 3 – MPI # [18] [20]) |  |  |
| REX 5.1C | Waterborne Light Industrial Coating | 1st | DSD [1] [2] [3] |
|  | (over alkyd primer) | 2nd | W.B. Light Industrial Coating |
|  | Gloss Level [G3] [G5] [G6] | 3rd | W.B. Light Industrial Coating |
|  | (DSD 2 or 3 – MPI # [23] [79]) |  |  |
| REX 5.1D | Alkyd | 1st | DSD [1] [2] [3] |
|  | Gloss Level [G1] [G5] [G6] | 2nd | Alkyd |
|  | (DSD 2 or 3 – MPI # [23] [79]) | 3rd | Alkyd |
| REX 5.1E | Epoxy, Water Based | 1st | DSD [1] [2] [3] |
|  | (DSD 2 or 3 – MPI # 107) | 2nd | W. B. Epoxy |
|  |  | 3rd | W. B. Epoxy |
| REX 5.1F | High Build Epoxy | 1st | DSD [1] [2] [3] |
|  | (DSD 2 or 3 – MPI # 101, [98] [108] as required) | 2nd | Epoxy |
|  |  | 3rd | Epoxy |
| REX 5.1G | Polyurethane, Pigmented | 1st | DSD [1] [2] [3] |
|  | (over epoxy zinc rich primer and high build epoxy) | 2nd | Polyurethane |
|  |  | 3rd | Polyurethane |
|  | (DSD 2 or 3 – MPI # [18] [20], 98 as required) |  |  |
| REX 5.1H | Polyurethane, Pigmented | 1st | DSD [1] [2] [3] |
|  | (over high build epoxy) | 2nd | Polyurethane |
|  | (DSD 2 or 3 – MPI # 101, [98] [108] as required) | 3rd | Polyurethane |
| REX 5.1J | Aluminum Paint | 1st | DSD [1] [2] [3] |
|  | (DSD 2 or 3 – MPI # [23] [79]) | 2nd | Aluminum Paint |
|  |  | 3rd | Aluminum Paint |
| REX 5.1K | Waterborne Light Industrial Coating | 1st | DSD [1] [2] [3] |
|  | (over w.b. primer) | 2nd | W.B. Light Industrial Coating |
|  | Gloss Level [G3] [G5] [G6] | 3rd | W.B. Light Industrial Coating |
|  | (DSD 2 or 3 – MPI # 107]) |  |  |
| REX 5.1L | Waterborne Light Industrial Coating | 1st | DSD [1] [2] [3] |
|  | (over epoxy primer) | 2nd | W.B. Light Industrial Coating |
|  | Gloss Level [G3] [G5] [G6] | 3rd | W.B. Light Industrial Coating |
|  | (DSD 2 or 3 – MPI # 101]) |  |  |
| REX 5.1M | Polyurethane, Pigmented | 1st | DSD [1] [2] [3] |
|  | (over zinc rich primer and epoxy) | 2nd | Polyurethane |
|  | (DSD 2 or 3 – MPI # [18] [20], 77 as required) | 3rd | Polyurethane |

REX 5.2 – STEEL – HIGH HEAT

| REX 5.2A | Heat Resistant Enamel | Heat Resistant Enamel, Apply in strict accordance with Manufacturer’s Instructions |
| --- | --- | --- |
|  | Maximum 205°C (400°F) |  |
| REX 5.2B | Heat Resistant Enamel, Aluminum | Aluminum Heat Resistant Enamel, Apply in strict accordance with Manufacturer’s Instructions |
|  | Maximum 427°C (800°F) |  |
| REX 5.2C | Inorganic Zinc Rich Coating | Inorganic Zinc Rich Coating, Apply in strict accordance with Manufacturer’s Instructions |
|  | Maximum 400°C (750°F) |  |
| REX 5.2D | High Heat Resistant Coating | High Heat Resistant Coating, Apply in strict accordance with Manufacturer’s Instructions |
|  | Maximum 593°C (1100°F) |  |

REX 5.3 – GALVANIZED METAL

| REX 5.3A | Latex | 1st | DSD [1] [2] [3] |
| --- | --- | --- | --- |
|  | Gloss Level [G1] [G5] [G6] | 2nd | Latex |
|  | (DSD 2 or 3 – MPI # 26) | 3rd | Latex |
| REX 5.3B | Alkyd | 1st | DSD [1] [2] [3] |
|  | Gloss Level [G1] [G5] [G6] | 2nd | Alkyd |
|  | (DSD 2 or 3 – MPI # 26) | 3rd | Alkyd |
| REX 5.3C | Epoxy | 1st | DSD [1] [2] [3] |
|  | (high contact / traffic) | 2nd | Epoxy |
|  | (DSD 2 or 3 – MPI # 101) | 3rd | Epoxy |
| REX 5.3D | Polyurethane, Pigmented | 1st | DSD [1] [2] [3] |
|  | (high contact / traffic) | 2nd | Polyurethane |
|  | (DSD 2 or 3 – MPI # 101) | 3rd | Polyurethane |
| REX 5.3E | Bituminous | 1st | DSD [1] [2] [3] |
|  | (low contact / traffic) | 2nd | Bituminous |
| REX 5.3F | Aluminum Paint | 1st | DSD [1] [2] [3] |
|  | (low contact / traffic) | 2nd | Aluminum Paint |
|  | (DSD 2 or 3 – MPI # 26) | 3rd | Aluminum Paint |
| REX 5.3G | Waterborne Light Industrial Coating | 1st | DSD [1] [2] [3] |
|  | Gloss Level [G3] [G5] [G6] | 2nd | W.B. Light Industrial Coating |
|  | (DSD 2 or 3 – MPI # 26) | 3rd | W.B. Light Industrial Coating |
| REX 5.3H | Latex (low contact / traffic) | 1st | DSD [1] [2] [3] |
|  | (over w.b. primer) | 2nd | Latex |
|  | Gloss Level [G1] [G5] [G6] | 3rd | Latex |
|  | (DSD 2 or 3 – MPI # 134) |  |  |
| REX 5.3J | Waterborne Light Industrial Coating | 1st | DSD [1] [2] [3] |
|  | (over w.b. primer) | 2nd | W.B. Light Industrial Coating |
|  | Gloss Level [G3] [G5] [G6] | 3rd | W.B. Light Industrial Coating |
|  | (DSD 2 or 3 – MPI # 134) |  |  |

REX 5.4 – ALUMINUM (non-anodized)

| REX 5.4A | Alkyd | 1st | DSD [1] [2] [3] |
| --- | --- | --- | --- |
|  | Gloss Level [G1] [G5] [G6] | 2nd | Alkyd |
|  | (DSD 2 or 3 – MPI # 95) | 3rd | Alkyd |
| REX 5.4B | Polyurethane, Pigmented | 1st | DSD [1] [2] [3] |
|  | (DSD 2 or 3 – MPI # 101) | 2nd | Polyurethane |
|  |  | 3rd | Polyurethane |
| REX 5.4C | Aluminum Paint | 1st | DSD [1] [2] [3] |
|  | (DSD 2 or 3 – MPI # 95) | 2nd | Aluminum Paint |
|  |  | 3rd | Aluminum Paint |
| REX 5.4D | Bituminous | 1st | DSD [1] [2] [3] |
|  |  | 2nd | Bituminous |
|  |  | 3rd | Bituminous |
| REX 5.4E | Epoxy | 1st | DSD [1] [2] [3] |
|  | (DSD 2 or 3 – MPI # 101) | 2nd | Epoxy |
|  |  | 3rd | Epoxy |
| REX 5.4F | Waterborne Light Industrial Coating | 1st | DSD [1] [2] [3] |
|  | Gloss Level [G3] [G5] [G6] | 2nd | W.B. Light Industrial Coating |
|  | (DSD 2 or 3 – MPI # 95) | 3rd | W.B. Light Industrial Coating |
| REX 5.4G | Latex | 1st | DSD [1] [2] [3] |
|  | Gloss Level [G1] [G5] [G6] | 2nd | Latex |
|  | (DSD 2 or 3 – MPI # 95) | 3rd | Latex |

REX 5.5 – COPPER (excluding roofs)

| REX 5.5A | Alkyd | 1st | DSD [1] [2] [3] |
| --- | --- | --- | --- |
|  | Gloss Level [G1] [G5] [G6] | 2nd | Alkyd |
|  | (DSD 2 or 3 – MPI # 95) | 3rd | Alkyd |
| REX 5.5B | Polyurethane, Pigmented | 1st | DSD [1] [2] [3] |
|  | (DSD 2 or 3 – MPI # 101) | 2nd | Polyurethane |
|  |  | 3rd | Polyurethane |
| REX 5.5C | Aluminum Paint | 1st | DSD [1] [2] [3] |
|  | (DSD 2 or 3 – MPI # 95) | 2nd | Aluminum Paint |
|  |  | 3rd | Aluminum Paint |
| REX 5.5D | Bituminous | 1st | DSD [1] [2] [3] |
|  |  | 2nd | Bituminous |
|  |  | 3rd | Bituminous |
| REX 5.5E | Epoxy | 1st | DSD [1] [2] [3] |
|  | (DSD 2 or 3 – MPI # 101) | 2nd | Epoxy |
|  |  | 3rd | Epoxy |
| REX 5.5F | Waterborne Light Industrial Coating | 1st | DSD [1] [2] [3] |
|  | Gloss Level [G3] [G5] [G6] | 2nd | W.B. Light Industrial Coating |
|  | (DSD 2 or 3 – MPI # 95) | 3rd | W.B. Light Industrial Coating |
| REX 5.5G | Latex | 1st | DSD [1] [2] [3] |
|  | Gloss Level [G1] [G5] [G6] | 2nd | Latex |
|  | (DSD 2 or 3 – MPI # 95) | 3rd | Latex |

REX 5.6 – STAINLESS STEEL (not polished)

| REX 5.6A | Alkyd | 1st | DSD [1] [2] [3] |
| --- | --- | --- | --- |
|  | Gloss Level [G1] [G5] [G6] | 2nd | Alkyd |
|  | (DSD 2 or 3 – MPI # 95) | 3rd | Alkyd |
| REX 5.6B | Polyurethane, Pigmented | 1st | DSD [1] [2] [3] |
|  | (DSD 2 or 3 – MPI # 101) | 2nd | Polyurethane |
|  |  | 3rd | Polyurethane |
| REX 5.6C | Aluminum Paint | 1st | DSD [1] [2] [3] |
|  | (DSD 2 or 3 – MPI # 95) | 2nd | Aluminum Paint |
|  |  | 3rd | Aluminum Paint |
| REX 5.6D | Epoxy | 1st | DSD [1] [2] [3] |
|  | (DSD 2 or 3 – MPI # 101) | 2nd | Epoxy |
|  |  | 3rd | Epoxy |
| REX 5.6E | Epoxy, Water Based | 1st | DSD [1] [2] [3] |
|  | (DSD 2 or 3 – MPI # 101) | 2nd | W. B. Epoxy |
|  |  | 3rd | W. B. Epoxy |
| REX 5.6F | Latex | 1st | DSD [1] [2] [3] |
|  | Gloss Level [G1] [G5] [G6] | 2nd | Latex |
|  | (DSD 2 or 3 – MPI # [69] [95]) | 3rd | Latex |
| REX 5.6G | Waterborne Light Industrial Coating | 1st | DSD [1] [2] [3] |
|  | Gloss Level [G3] [G5] [G6] | 2nd | W.B. Light Industrial Coating |
|  | (DSD 2 or 3 – MPI # 95) | 3rd | W.B. Light Industrial Coating |

REX 6.1 – GLUE LAMINATED BEAMS AND COLUMNS

| REX 6.1A | Latex | 1st | DSD [1] [2] [3] |
| --- | --- | --- | --- |
|  | (over alkyd primer) | 2nd | Latex |
|  | Gloss Level [G1] [G5] [G6] | 3rd | Latex |
|  | (DSD 2 or 3 – MPI # 5) |  |  |
| REX 6.1B | Alkyd | 1st | DSD [1] [2] [3] |
|  | Gloss Level [G1] [G5] [G6] | 2nd | Alkyd |
|  | (DSD 2 or 3 – MPI # 5) | 3rd | Alkyd |
| REX 6.1C | Solid Colour Stain | 1st | DSD [1] [2] [3] |
|  | (DSD 2 or 3 – MPI # 5) | 2nd | Solid Colour Stain |
|  |  | 3rd | Solid Colour Stain |
| REX 6.1D | Semi-transparent Stain | 1st | DSD [1] [2] [3] |
|  |  | 2nd | Semi-transparent Stain |
|  |  | 3rd | Semi-transparent Stain |
| REX 6.1E | Polyurethane, Clear, 2 Component | 1st | DSD [1] [2] [3] |
|  |  | 2nd | Polyurethane |
|  |  | 3rd | Polyurethane |
| REX 6.1F | Polyurethane, Pigmented | 1st | DSD [1] [2] [3] |
|  | (DSD 2 or 3 – MPI # 77) | 2nd | Polyurethane |
|  |  | 3rd | Polyurethane |
| REX 6.1G | Varnish | 1st | DSD [1] [2] [3] |
|  | Gloss Level [G5] [G6] | 2nd | Varnish |
|  |  | 3rd | Varnish |
|  |  | 4th | Varnish |
| REX 6.1H | Varnish | 1st | DSD [1] [2] [3] |
|  | (over stain) | 2nd | Varnish |
|  | Gloss Level [G5] [G6] | 3rd | Varnish |
|  | (DSD 2 or 3 – MPI # 13) | 4th | Varnish |
| REX 6.1J | Polyurethane, Clear, 2 Component | 1st | DSD [1] [2] [3] |
|  | (over stain) | 2nd | Polyurethane |
|  | (DSD 2 or 3 – MPI # 13) | 3rd | Polyurethane |
|  |  | 4th | Polyurethane |
| REX 6.1K | Fire Retardant, Pigmented | (ULC approved), Apply in strict accordance with Manufacturer’s Instructions |
| REX 6.1L | Latex | 1st | DSD [1] [2] [3] |
|  | (over latex primer) | 2nd | Latex |
|  | Gloss Level [G1] [G5] [G6] | 3rd | Latex |
|  | (DSD 2 or 3 – MPI # 6) |  |  |

REX 6.2 – DIMENSION LUMBER

| REX 6.2A | Latex | 1st | DSD [1] [2] [3] |
| --- | --- | --- | --- |
|  | Gloss Level [G1] [G5] [G6] | 2nd | Latex |
|  | (DSD 2 or 3 – MPI # [5] [6]) | 3rd | Latex |
| REX 6.2B | Solid Colour Stain, Waterborne. | 1st | DSD [1] [2] [3] |
|  | (DSD 2 or 3 – MPI # [5] [6]) | 2nd | Latex Stain |
|  |  | 3rd | Latex Stain |
| REX 6.2C | Alkyd | 1st | DSD [1] [2] [3] |
|  | Gloss Level [G1] [G5] [G6] | 2nd | Alkyd |
|  | (DSD 2 or 3 – MPI # 5) | 3rd | Alkyd |
| REX 6.2D | Solid Colour Stain | 1st | DSD [1] [2] [3] |
|  | (DSD 2 or 3 – MPI # 5) | 2nd | Solid Colour Stain |
|  |  | 3rd | Solid Colour Stain |
| REX 6.2E | Semi-transparent Stain | 1st | DSD [1] [2] [3] |
|  |  | 2nd | Semi-transparent Stain |
| REX 6.2F | Fire Retardant, Pigmented | (ULC approved), Apply in strict accordance with Manufacturer’s Instructions |
| REX 6.2G | Polyurethane, Clear, 2 Component | 1st | DSD [1] [2] [3] |
|  |  | 2nd | Polyurethane |
|  |  | 3rd | Polyurethane |
| REX 6.2H | Polyurethane, Pigmented | 1st | DSD [1] [2] [3] |
|  |  | 2nd | Polyurethane |
|  |  | 3rd | Polyurethane |
| REX 6.1J | Varnish | 1st | DSD [1] [2] [3] |
|  | Gloss Level [G5] [G6] | 2nd | Varnish |
|  |  | 3rd | Varnish |
|  |  | 4th | Varnish |
| REX 6.1K | Latex Transition System | 1st | Alkyd Primer |
|  | (over alkyd primer) | 2nd | Latex |
|  | Gloss Level [G1] [G5] [G6] | 3rd | Latex |

REX 6.3 – DRESSED LUMBER

| REX 6.3A | Latex | 1st | DSD [1] [2] [3] |
| --- | --- | --- | --- |
|  | Gloss Level [G1] [G5] [G6] | 2nd | Latex |
|  | (do not use G1 on doors) | 3rd | Latex |
|  | (DSD 2 or 3 – MPI # 5) |  |  |
| REX 6.3B | Alkyd | 1st | DSD [1] [2] [3] |
|  | Gloss Level [G1] [G5] [G6] | 2nd | Alkyd |
|  | (do not use G1 on doors) | 3rd | Alkyd |
|  | (DSD 2 or 3 – MPI # 5) |  |  |
| REX 6.3C | Solid Colour Stain | 1st | DSD [1] [2] [3] |
|  | (not for high contact or doors) | 2nd | Solid Colour Stain |
|  | (DSD 2 or 3 – MPI # 5) | 3rd | Solid Colour Stain |
| REX 6.3D | Semi-transparent Stain | 1st | DSD [1] [2] [3] |
|  | (not for use on doors) | 2nd | Semi-transparent Stain |
|  |  | 3rd | Semi-transparent Stain |
| REX 6.3E | Varnish | 1st | DSD [1] [2] [3] |
|  | (over stain) | 2nd | Varnish |
|  | Gloss Level [G5] [G6] | 3rd | Varnish |
|  | (DSD 2 or 3 – MPI # 13) | 4th | Varnish |
| REX 6.3F | Varnish | 1st | DSD [1] [2] [3] |
|  | Gloss Level [G5] [G6] | 2nd | Varnish |
|  |  | 3rd | Varnish |
|  |  | 4th | Varnish |
| REX 6.3G | Polyurethane, Clear, 2 Component | 1st | DSD [1] [2] [3] |
|  |  | 2nd | Polyurethane |
|  |  | 3rd | Polyurethane |
| REX 6.3H | Polyurethane, Pigmented | 1st | DSD [1] [2] [3] |
|  |  | 2nd | Polyurethane |
|  |  | 3rd | Polyurethane |
| REX 6.3J | Waterborne Light Industrial Coating | 1st | DSD [1] [2] [3] |
|  | Gloss Level [G5] [G6] | 2nd | W. B. Light Industrial Coating |
|  | (DSD 2 or 3 – MPI # 5) | 3rd | W. B. Light Industrial Coating |
| REX 6.3K | Solid Colour Stain, Waterborne | 1st | DSD [1] [2] [3] |
|  | (do not use on doors) | 2nd | Latex Stain |
|  | (DSD 2 or 3 – MPI # [5] [6]) | 3rd | Latex Stain |
| REX 6.3L | Latex | 1st | DSD [1] [2] [3] |
|  | (over latex primer) | 2nd | Latex |
|  | Gloss Level [G1] [G5] [G6] | 3rd | Latex |
|  | (DSD 2 or 3 – MPI # 6) |  |  |

REX 6.4 – WOOD PANELING

| REX 6.4A | Latex | 1st | DSD [1] [2] [3] |
| --- | --- | --- | --- |
|  | Gloss Level [G1] [G5] [G6] | 2nd | Latex |
|  | (DSD 2 or 3 – MPI # 5) | 3rd | Latex |
| REX 6.4B | Alkyd | 1st | DSD [1] [2] [3] |
|  | Gloss Level [G1] [G5] [G6] | 2nd | Alkyd |
|  | (DSD 2 or 3 – MPI # 5) | 3rd | Alkyd |
| REX 6.4C | Solid Colour Stain | 1st | DSD [1] [2] [3] |
|  | (DSD 2 or 3 – MPI # 5) | 2nd | Solid Colour Stain |
|  |  | 3rd | Solid Colour Stain |
| REX 6.4D | Semi-transparent Stain | 1st | DSD [1] [2] [3] |
|  |  | 2nd | Semi-transparent Stain |
| REX 6.4E | Fire Retardant, Pigmented | (ULC approved), Apply in strict accordance with Manufacturer’s Instructions |
| REX 6.4F | Fire Retardant, Penetrating Wood Preservative, Clear | (ULC approved), Apply in strict accordance with Manufacturer’s Instructions |
| REX 6.4G | Solid Colour Stain, Waterborne | 1st | DSD [1] [2] [3] |
|  | (DSD 2 or 3 – MPI # [5] [6]) | 2nd | Latex Stain |
|  |  | 3rd | Latex Stain |
| REX 6.4H | Varnish | 1st | DSD [1] [2] [3] |
|  | Gloss Level [G5] [G6] | 2nd | Varnish |
|  |  | 3rd | Varnish |
|  |  | 4th | Varnish |
| REX 6.4J | Varnish | 1st | DSD [1] [2] [3] |
|  | (over stain) | 2nd | Varnish |
|  | Gloss Level [G5] [G6] | 3rd | Varnish |
|  | (DSD 2 or 3 – MPI # 13) | 4th | Varnish |
| REX 6.4K | Latex | 1st | DSD [1] [2] [3] |
|  | (over latex primer) | 2nd | Latex |
|  | Gloss Level [G1] [G5] [G6] | 3rd | Latex |
|  | (DSD 2 or 3 – MPI # 6) |  |  |

REX 6.5 – WOOD DECKS AND STAIRS/STEPS

| REX 6.5A | Latex Porch & Floor | 1st | DSD [1] [2] [3] |
| --- | --- | --- | --- |
|  | (over alkyd primer) | 2nd | Latex Porch & Floor |
|  | Gloss level [G3] [G6] | 3rd | Latex Porch & Floor |
|  | [Anti-skid additive] |  |  |
|  | (DSD 2 or 3 – MPI # 5) |  |  |
| REX 6.5B | Alkyd Floor Enamel | 1st | DSD [1] [2] [3] |
|  | Gloss level [G4] [G6] | 2nd | Alkyd Floor Enamel |
|  | [Anti-skid Additive] | 3rd | Alkyd Floor Enamel |
| REX 6.5C | Deck Stain | 1st | DSD [1] [2] [3] |
|  |  | 2nd | Deck Stain |
| REX 6.5D | Non-slip Epoxy Deck Coating | Non-slip Epoxy Deck Coating, Apply in strict accordance with Manufacturer’s Instructions |
|  | (for plywood decks) |  |
| REX 6.5E | Latex Deck Coating | Latex Deck Coating, Apply in strict accordance with Manufacturer’s Instructions |
|  | (for plywood decks) |  |
| REX 6.5F | Latex Porch & Floor | 1st | DSD [1] [2] [3] |
|  | (over latex primer) | 2nd | Latex Porch & Floor |
|  | Gloss level [G3] [G6] | 3rd | Latex Porch & Floor |
|  | [Anti-skid Additive] |  |  |
|  | (DSD 2 or 3 – MPI # 6) |  |  |

REX 6.6 – WOOD SHINGLE AND SHAKE SIDING (excluding roofs)

| REX 6.6A | Latex | 1st | DSD [1] [2] [3] |
| --- | --- | --- | --- |
|  | Gloss Level [G1] [G5] [G6] | 2nd | Latex |
|  | (DSD 2 or 3 – MPI # 5) | 3rd | Latex |
| REX 6.6B | Alkyd | 1st | DSD [1] [2] [3] |
|  | Gloss Level [G1] [G5] [G6] | 2nd | Alkyd |
|  | (DSD 2 or 3 – MPI # 5) | 3rd | Alkyd |
| REX 6.6C | Solid Colour Stain | 1st | DSD [1] [2] [3] |
|  | (DSD 2 or 3 – MPI # [5] [7]) | 2nd | Solid Colour Stain |
|  |  | 3rd | Solid Colour Stain |
| REX 6.6D | Solid Colour Stain, Waterborne | 1st | DSD [1] [2] [3] |
|  | (DSD 2 or 3 – MPI # [5] [6] [7]) | 2nd | Latex Stain |
|  |  | 3rd | Latex Stain |
| REX 6.6E | Latex | 1st | DSD [1] [2] [3] |
|  | (over latex primer) | 2nd | Latex |
|  | Gloss Level [G1] [G5] [G6] | 3rd | Latex |
|  | (DSD 2 or 3 – MPI # 6) |  |  |
| REX 6.6F | Semi-transparent Stain | 1st | DSD [1] [2] [3] |
|  |  | 2nd | Semi-transparent Stain |

REX 6.7 – FIBERGLASS

| REX 6.7A | Latex | 1st | DSD [1] [2] [3] |
| --- | --- | --- | --- |
|  | Gloss Level [G1] [G5] [G6] | 2nd | Latex |
|  | (DSD 2 or 3 – MPI # 69) | 3rd | Latex |
| REX 6.7B | Alkyd | 1st | DSD [1] [2] [3] |
|  | Gloss Level [G1] [G5] [G6] | 2nd | Alkyd |
|  | (DSD 2 or 3 – MPI # 69) | 3rd | Alkyd |
| REX 6.7C | Waterborne Light Industrial Coating | 1st | DSD [1] [2] [3] |
|  | Gloss Level [G3] [G5] [G6] | 2nd | W. B. Light Industrial Coating |
|  | (DSD 2 or 3 – MPI # 69) | 3rd | W. B. Light Industrial Coating |
| REX 6.7D | Polyurethane, Pigmented | 1st | DSD [1] [2] [3] |
|  | (over epoxy) | 2nd | Polyurethane |
|  | (DSD 2 or 3 – MPI # 77) | 3rd | Polyurethane |
| REX 6.7E | Epoxy, Water Based | 1st | DSD [1] [2] [3] |
|  |  | 2nd | W. B. Epoxy |
|  |  | 3rd | W. B. Epoxy |
| REX 6.7F | Epoxy | 1st | DSD [1] [2] [3] |
|  |  | 2nd | Epoxy |
|  |  | 3rd | Epoxy |

REX 6.8 – PLASTIC

| REX 6.7A | Latex | 1st | DSD [1] [2] [3] |
| --- | --- | --- | --- |
|  | Gloss Level [G1] [G5] [G6] | 2nd | Latex |
|  | (DSD 2 or 3 – MPI # [17] [69]) | 3rd | Latex |
| REX 6.7B | Alkyd | 1st | DSD [1] [2] [3] |
|  | Gloss Level [G1] [G5] [G6] | 2nd | Alkyd |
|  | (DSD 2 or 3 – MPI # [17] [69]) | 3rd | Alkyd |
| REX 6.7C | Waterborne Light Industrial Coating | 1st | DSD [1] [2] [3] |
|  | Gloss Level [G3] [G5] [G6] | 2nd | W. B. Light Industrial Coating |
|  | (DSD 2 or 3 – MPI # [17] [69]) | 3rd | W. B. Light Industrial Coating |

REX 9.1 - STUCCO

| REX 9.1A | Latex | 1st | DSD [1] [2] [3] |
| --- | --- | --- | --- |
|  | Gloss Level [G1] [G5] [G6] | 2nd | Latex |
|  |  | 3rd | Latex |
| REX 9.1B | Waterborne Light Industrial Coating | 1st | DSD [1] [2] [3] |
|  | Gloss Level [G3] [G5] [G6] | 2nd | W. B. Light Industrial Coating |
|  |  | 3rd | W. B. Light Industrial Coating |
| REX 9.1C | Elastomeric | Elastomeric Coating, Apply in strict accordance with manufacturer’s instructions. |
| REX 9.1D | Epoxy | 1st | DSD [1] [2] [3] |
|  |  | 2nd | Epoxy |
|  |  | 3rd | Epoxy |
| REX 9.1E | Water Repellent | Water Repellent, Apply in strict accordance with manufacturer’s instructions. |
|  | (paintable) |  |
| REX 9.1F | High Build Latex | High Build Latex, Apply in strict accordance with manufacturer’s instructions. |
| REX 9.1G | Epoxy, Water Based | 1st | DSD [1] [2] [3] |
|  |  | 2nd | W. B. Epoxy |
|  |  | 3rd | W. B. Epoxy |
| REX 9.1H | Water Repellent | Water Repellent, Apply in strict accordance with manufacturer’s instructions. |
|  | (not paintable) |  |
| REX 9.1J | Latex (over alkali resistant primer) | 1st | DSD [1] [2] [3] |
|  | Gloss level [G1] [G5] [G6] | 2nd | Latex |
|  | (DSD 2 or 3 – MPI # 3) | 3rd | Latex |

REX 10.1 – CANVAS AND COTTON COVERINGS

| REX 10.1A | Latex | 1st | DSD [1] [2] [3] |
| --- | --- | --- | --- |
|  | Gloss Level [G1] [G5] [G6] | 2nd | Latex |
|  |  | 3rd | Latex |
| REX 10.1B | Waterborne Light Industrial Coating | 1st | DSD [1] [2] [3] |
|  | Gloss Level [G3] [G5] [G6] | 2nd | W. B. Light Industrial Coating |
|  |  | 3rd | W. B. Light Industrial Coating |
| REX 10.1C | Alkyd | 1st | DSD [1] [2] [3] |
|  | Gloss Level [G1] [G5] [G6] | 2nd | Alkyd |
|  | (DSD 2 or 3 – MPI # 10) | 3rd | Alkyd |
| REX 10.1D | Aluminum Paint | 1st | DSD [1] [2] [3] |
|  | (DSD 2 or 3 – MPI # 10) | 2nd | Aluminum Paint |
|  |  | 3rd | Aluminum Paint |

REX 10.2 – BITUMINOUS COATED SURFACES

| REX 10.2A | Latex | 1st | DSD [1] [2] [3] |
| --- | --- | --- | --- |
|  | Gloss Level [G1] [G5] [G6] | 2nd | Latex |
|  | (DSD 2 or 3 – MPI # 107) | 3rd | Latex |
| REX 10.2B | Latex Aggregate, [Coarse] [Medium] texture, Gloss level [G1] [G5] [G6] | Latex Aggregate, Apply in strict accordance with manufacturer’s instructions. |
| REX 10.1C | Alkyd | 1st | DSD [1] [2] [3] |
|  | Gloss Level [G1] [G5] [G6] | 2nd | Alkyd |
|  | (DSD 2 or 3 – MPI # 107) | 3rd | Alkyd |
| REX 10.1D | Aluminum Paint | 1st | DSD [1] [2] [3] |
|  | (DSD 2 or 3 – MPI # 107) | 2nd | Aluminum Paint |
|  |  | 3rd | Aluminum Paint |

# END OF SECTION