Section Cover Page

Section 10 28 13 2011-08-24 Washroom Accessories

Refer to “LEED Notes and Credits” page for additional guidance for LEED projects. Delete LEED items if project: .1 is excluded by the Department’s policy on LEED, or .2 the Department has determined that the work of this Contract is not to attain a LEED rating.

This Master Specification Section contains:

.1	This Cover Sheet

.2	LEED Notes and Credits

.3	Specification Section Text:

1.	General

1.1	Related Work Specified in Other Sections

1.2	Reference Documents

1.3	Submittals

1.4	Closeout Submittals

1.5	Maintenance Material Submittals

1.6	Delivery, Storage, and Handling

2.	Products

2.1	Fixtures

2.2	Shower and Dressing Accessories

3.	Execution

3.1	Installation

3.2	Location and Quantity

LEED Notes:

N/A

LEED Credits:

Contribution towards LEED credits in this section may apply as follows:

1.	LEED Credit MR 4: Recycled Content.

.1	The criteria is that the sum of post-consumer recycled content plus one-half of the pre-consumer content constitutes at least the percent(10% and 20%)of the total value of the materials in the project. Metal in washroom accessory products may contain recycled material. For example, steel, aluminum and stainless steel have post industrial as well as post consumer recycled components. Product data and/or LEED letters from manufacturers are required for verification..

2.	MR Credit 5 Regional Materials:

.1	Use building materials or products that have been extracted, harvested, recovered and processed within 800 km (2400 km is shipped by rail or water) of the final manufacturing site.  Demonstrate that the final manufacturing site is within 800 km (2400 km is shipped by rail or water) of the project site for these products. If fabricated regionally, products specified will count in this credit. The contractor will be required to submit documentation consisting of cost, weight, transportation service and distances as evidence of compliance with credit requirements.

1.	General

1.1	RELATED Work Specified in Other SECTIONS

.1	[LEED Submittal Forms	Section 01 32 16]

.2	[LEED Requirements	Section 01 35 18]

.3	[Environmental Procedures	Section 01 35 20]

.4	Waste Management and Disposal	Section 01 74 19

.5	Mirror Glass:	Section 08 83 13

.6	Ceramic bath accessories:	Section 09 30 13

.7	Metal Washroom Partitions:	Section 10 21 13

.8	Plastic Laminate Washroom Partitions:	Section 10 21 14

1.2	reference Documents

SPEC NOTE: Edit this article to include only standards referenced within the edited version of this Section, including LEED documentation and sustainable practices.

.1	American Society for Testing and Materials (ASTM):

| .1 | ASTM A167 99 (2009) | Standard Specification for Stainless and Heat Resisting Chromium Nickel Steel Plate, Sheet, and Strip |
| --- | --- | --- |
| .2 | ASTM B456-03 (2009) | Standard Specification for Electrodeposited Coatings of Copper Plus Nickel Plus Chromium and Nickel Plus Chromium |
| .3 | ASTM A653/ A653M-09 | Standard Specification for Steel Sheet, Zinc Coated (Galvanized) or Zinc Iron Alloy Coated (Galvannealed) by the Hot Dip Process |
| .4 | ASTM A666-03 | Standard Specification for Annealed or Cold-Worked Austenitic Stainless Steel Sheet, Strip, Plate, and Flat Bar |
| .5 | ASTM A924/ A924M-09 | Standard Specification for General Requirements for Steel Sheet, Metallic Coated by the Hot Dip Process |

.2	Canada Green Building Council (CaGBC):

| .1 | LEED Canada 2009 Rating System | LEED Canada for New Construction and Major Renovations. LEED Canada for Core and Shell Development. Website: www.cagbc.org] |
| --- | --- | --- |

.3	Canadian General Standards Board (CGSB):

| .1 | CAN/CGSB 1.36-97 | General Purpose Interior Varnish |
| --- | --- | --- |
| .2 | CAN/CGSB 1.81-M90 | Air Drying and Baking Alkyd Primer for Vehicles and Equipment |
| .3 | CAN/CGSB 1.88-92 | Gloss Alkyd Enamel, Air Drying and Baking |
| .4 | CGSB 31 GP 107MA 1990 | Non inhibited Phosphoric Acid Base Metal Conditioner and Rust Remover |

.4	Canadian Standards Association (CSA):

| .1 | CAN/CSA G164-R2003 | Hot Dip Galvanizing of Irregularly Shaped Articles |
| --- | --- | --- |

1.3	SUBMITTALS

.1	Product Data:

.1	Submit manufacturer’s printed product literature, specifications and data sheets in accordance with Section 01 33 00 - Submittal Procedures.

.2	Shop Drawings:

.1	Submit shop drawings or catalogue illustrations in accordance with Division 01.

.3	Samples:

.1	Submit samples in accordance with Section [01 33 00 - Submittal Procedures].

.2	Samples to be returned for inclusion into work.

.4	Sustainable Design Submittals:

SPEC NOTE: Use the following paragraph when LEED Submittals are required:

.1	LEED Submittals: Submit documentation in accordance with Section 01 35 18 – LEED Requirements.  Submit documentation for the following:

.1	Materials & Resources:

SPEC NOTE: Delete LEED submittal item if project is not to attain LEED certification or if Credit MR 4 is not being sought.

.1	MR Credit 4 - Recycled Content: [10%] [20%] (post-consumer + ½ pre-consumer).

SPEC NOTE: Delete LEED submittal item if project is not to attain LEED certification or if Credit MR 5 is not being sought.

.3	MR Credit 5 - Regional Materials: [20%] [30%] Extracted and Manufactured Regionally.

1.4	Closeout submittals

.1	Operation and Maintenance Data:

.1	Provide maintenance data for toilet and bath accessories for incorporation into manual specified in Section 01 78 00 - Closeout Submittals.

1.5	maintenance material submittals

.1	Tools:

.1	Provide special tools required for accessing, assembly/disassembly or removal for toilet and bath accessories in accordance with requirements specified in Section 01 78 00 - Closeout Submittals.

.2	Deliver special tools to Minister.

1.6	Delivery, storage, and handling

.1	Waste Management and Disposal:

.1	Separate waste materials for [reuse] [and] [recycling] in accordance with Section 01 74 19 – Management and Disposal.

2.	Products

2.1	FIXTURES

.1	Soap Dispenser:  Recessed type.  minimum 0.8 mm stainless steel door and covered soap tank, minimum  1100 mL capacity.  Soap tank attached to minimum  0.8 mm galvanized steel wall box with continuous stainless steel hinge.  Stainless steel soap valve mechanism.  Soap level indicator.

.2	Tissue Dispenser:  wall mounted, 1.2 mm steel with chrome finish, double roll dispenser.  Tension spring and self locking device.

.3	Combination Paper Towel and Disposal Unit:  for recessed installation, fabricated from 1.3 mm x 302 stainless steel having #4 finish for towel and waste access doors, with other surfaces fabricated from 1.0 mm and 0.8 mm x 302 stainless steel having #4 finish.  Waste receptacle to have removable 0.6 mm satin zinc coated steel liner.  Towel cradle and wallbox fabricated from 0.8 mm zinc coated steel, adjustable to accommodate paper towels of single, multi or roll applications.

.4	Napkin Dispenser:  coin operated, surface mounted, fabricated from 0.9 mm cold rolled steel with white baked enamel finish.  Piano hinge to door.  Dispenser to be provided with door lock and theft guard to chute.  Unit to dispense the standard napkin product.

.5	Feminine Napkin Disposal:  recessed type, 0.8 mm Type 302 stainless steel, one piece coverall door and receptacle bin, which shall be removable for maintenance and cleaning.  Wall box fabricated from 0.8 mm satin coat galvanized steel with deodorant block and holder.  Graphic on front of unit.

.6	Grab Bars:  32 mm dia. x 1.5 mm wall tubing of stainless steel, [concealed] screw attachment, flanges welded to tubular bar, provided with steel back plates and all accessories.  [Knurl bar at area of hand grip].

.7	Towel Bars:  19 mm [diameter] [or] [square] stainless tubing, chrome plated cast bronze end brackets, concealed fasteners, [482 mm] [610 mm] [762 mm] long.

2.6	SHOWER AND DRESSING ACCESSORIES

.1	Curtain Rods:  [stainless steel or chrome-plated brass] [chrome-plated steel] tubing, 32 mm diameter, minimum 1.2 mm wall thickness, with 76 mm dia. chrome plated cast brass flanges each end for attachment to wall.

SPEC NOTE:  Specify stainless steel or chrome-plated brass rods for installations exposed to moisture or high humidity.

.2	Curtains:  [opaque vinyl] [anti-bacterial, fire resistive, self-extinguishing vinyl laminated fabric], matte finish, minimum 180 micrometre thick, with grommets of stainless steel or nickel-plated brass for curtain hooks.

.3	Curtain Hooks:  stainless steel, sized to suit rods.

.4	Curtain holdback hooks and chains:  stainless steel or chrome-plated brass.

.5	[Dressing] [and] [Shower] Compartment Seats:  [Solid] [Composite] [Plastic laminate] [laminated hardwood with varnish finish to CAN/CGSB-1.36].

.6	Seat Supports:  Stainless steel to ASTM A666 [Type 302], polished finish.

.7	Shower Seat Sealer:  Water resistant sealer or glue acceptable to laminate manufacturer.

.8	Towel and Robe Hooks:  Stainless steel, double hook, flush tamper proof fasteners.

.9	Soap Trays:  surface mounted, 5 mm thick stainless steel dished tray, self draining, flush screw.

3.	Execution

3.1	INSTALLATION

.1	Install and secure all fixtures rigidly in place using the following techniques.

.1	For stud walls install steel back plate to stud prior to plaster or drywall finish.  Plate to have threaded studs or plugs provided.

.2	For hollow masonry units or existing plaster/drywall surfaces use toggle bolts drilled into cell/wall cavity.

.3	In solid masonry, marble, stone or concrete use bolt with lead expansion sleeve set into drilled hole.

.4	In [toilet] [and] [shower] compartment partitions, use male/female through bolts.

.2	For installation of grab bars to metal toilet partitions, provide templates and detail to partition manufacturer for shop fabrication of steel reinforcing plates.  Instruct whether shop or field, drill and tap technique will be used.

.3	Use tamper proof headed [screws] [and] [bolts] for fasteners.

3.2	LOCATION AND QUANTITY

.1	Locate accessories [where indicated on drawings], [and as follows].  Exact locations to be determined by Minister.

.2	Toilet tissue dispenser:  one in each toilet compartment.

.3	Paper towel dispenser:  [one in each washroom] [one per 2 wash basins].

.4	Combination paper towel and disposal unit:  [one] [in each washroom] [where indicated on drawings].

.5	Soap dispenser:  [one over each lavatory] [one per 2 wash basins].

.6	Feminine napkin dispenser:  one for each female washroom.

.7	Feminine napkin disposal bin:  one in each female toilet compartment.

.8	Shower curtain:  one at each shower compartment.

.9	Soap tray:  one at each shower unit.

.10	Towel bar:  one adjacent to each shower unit.

.11	Grab bar:  two in each toilet compartment designed for handicapped.

.12	Towel and robe hooks:  two for each shower compartment [as indicated on drawings].

.13	Curtain holdback hook and chain:  one at each shower curtain.

END OF SECTION