Section Cover Page

Section 10 51 00 2011-08-24 Lockers

Refer to “LEED Notes and Credits” page for additional guidance for LEED projects. Delete LEED items if project: .1 is excluded by the Department’s policy on LEED, or .2 the Department has determined that the work of this Contract is not to attain a LEED rating.

Use this Section to specify requirements for factory fabricated metal clothing lockers and lockerettes.

This Master Specification Section contains:

.1	This Cover Sheet

.2	LEED Notes and Credits

.3	Specification Section Text:

1.	General

1.1	Related Work Specified in Other Sections

1.2	Reference Documents

1.3	Product Options and Substitutions

1.4	Submittals

1.5	Delivery, Storage, and Handling

2.	Products

2.1	Materials

3.	Execution

3.1	Installation

If locker units are integrally ventilated by a mechanical system, co-ordinate mechanical and specifications with this section.

LEED Notes:

N/A

LEED Credits:

Contribution towards LEED credits in this section may apply as follows:

1.	LEED Credit MR 4: Recycled Content.

.1	The criteria is that the sum of post-consumer recycled content plus one-half of the pre-consumer content constitutes at least the percent(10% and 20%) of the total value of the materials in the project. Metal locker products contain recycled material. For example, steel, aluminum and stainless steel have post industrial as well as post consumer recycled components.

2.	MR Credit 5 Regional Materials:

.1	Use building materials or products that have been extracted, harvested, recovered and processed within 800 km (2400 km is shipped by rail or water) of the final manufacturing site.  Demonstrate that the final manufacturing site is within 800 km (2400 km is shipped by rail or water) of the project site for these products. If fabricated regionally, products specified will count towards this credit. The contractor will be required to submit documentation consisting of cost, weight, transportation service and distances as evidence of compliance with credit requirements.

1.	General

1.1	RELATED WORK SPECIFIED IN OTHER SECTIONS

.1	[LEED Submittal Forms	Section 01 32 16]

.2	[LEED Requirements	Section 01 35 18]

.3	[Environmental Procedures	Section 01 35 20]

.4	Waste Management and Disposal	Section 01 74 19

.5	Concrete Bases:	Section 03 30 00

.6	Wood grounds and nailing strips:	Section 06 10 00

.7	Ductwork and connections to exhaust system:	Division 23

1.2	REFERENCE Documents

SPEC NOTE: Edit this article to include only standards referenced within the edited version of this Section, including LEED documentation and sustainable practices.

.1	American Society for Testing and Materials (ASTM):

| .1 | ASTM A167-99(2009) | Specification for Stainless and Heat Resisting Chromium Nickel Steel Plate, Sheet and Strip |
| --- | --- | --- |
| .2 | ASTM A653/ A653M-09 | Specification for Steel Sheet, Zinc Coated (Galvanized) or Zinc Iron Alloy Coated (Galvannealed) by the Hot Dip Process |
| .3 | ASTM A924 /A924M-09 | Specification for General Requirements for Steel Sheet, Metallic Coated by the Hot Dip Process |

.2	Canada Green Building Council (CaGBC):

| .1 | LEED Canada 2009 Rating System | LEED Canada for New Construction and Major Renovations. LEED Canada for Core and Shell Development. Website: www.cagbc.org] |
| --- | --- | --- |

.3	Canadian General Standards Board (CGSB):

| .1 | CAN/CGSB-44.40-2001 | Steel Clothing Locker |
| --- | --- | --- |

1.3	PRODUCT OPTIONS AND SUBSTITUTIONS

.1	Refer to Division 01 for requirements pertaining to product options and substitutions.

1.4	submittals

.1	Product Data:

.1	Submit manufacturer’s printed product literature, specifications and data sheets in accordance with Section 01 33 00 - Submittal Procedures.

.2	Shop Drawings:

.1	Submit shop drawings in accordance with Division 01.

.2	Indicate thicknesses of metal, fabricating  methods, [assembled banks of lockers], bases] [trim] [numbering] [filler panels] [end/back panels].

.3	Samples:

.1	Submit sample of colour and finish on actual base metal in accordance with Division 01.

.4	Sustainable Design Submittals:

SPEC NOTE: Use the following paragraph when LEED Submittals are required:

.1	LEED Submittals: Submit documentation in accordance with Section 01 35 18 – LEED Requirements.  Submit documentation for the following:

.1	Materials & Resources:

SPEC NOTE: Delete LEED submittal item if project is not to attain LEED certification or if Credit MR 4 is not being sought.

.1	MR Credit 4 - Recycled Content: [10%] [20%] (post-consumer + ½ pre-consumer)

SPEC NOTE: Delete LEED submittal item if project is not to attain LEED certification or if Credit MR 5 is not being sought.

.2	MR Credit 5 - Regional Materials: [20%] [30%] Extracted and Manufactured Regionally

1.5	delivery, storage, and handling

.1	Waste Management and Disposal:

.1	Separate waste materials for [reuse] [and] [recycling] in accordance with Section 01 74 19 – Management and Disposal.

2.	Products

2.1	MATERIALS

.1	Lockers:  to CAN/CGSB-44.40, Type [     ] [Class     ]. [Banks of lockers indicated].

SPEC NOTE 	Type 	 W 	 D 	  H

1	305	380	1830 mm

2	305	457	1830

3	380	457	1830

4	380	533	1830

SPEC NOTE 	Class 	Description

1	One complete locker.

2	A bank of two lockers.

3	A bank of three lockers.

4	A bank of four lockers.

5	A bank of five lockers.

.1	[Single tier] [Double tier] [Free standing] [recessed] with [single] [double] wall construction, [flush with] [proud from frame], [bright] [painted] [metal] [plastic] recessed handle/lock pockets] bright metal handles, number plates, [[     ] shelves] [[     ] coat hooks] [[skirt] [leg] base], [wall trim] [filler panels/false front], [welded construction] [K.D. construction], [sloping tops] [plenum panels], [finish] end/back panels], in baked enamel finish.

.2	Lockerettes to CAN/CGSB-44.40 [    ] mm wide x [     ] mm deep x [     ] mm high.

.1	Arranged as indicated with doors of [single] [double wall] construction, [[bright] [painted] [plastic] metal] recessed handle and lock pockets], bright metal handles, number plates, [wall trim] [sloping tops] [welded] [K.D] construction, in baked enamel finish.

.3	Locking system:  [padlocks] [cylinder locks] [built-in combination locks] [supplied by locker manufacturer] [as specified in Section 08 70 00].

SPEC NOTE:  If cylinder locks are specified, includes keeping system and number of keeps.

3.	Execution

3.1	INSTALLATION

.1	Assembly and install lockers.

.2	Secure locker to wall with expansion bolts or to wood grounds and nailing strips.  Inter-bolt locker units together.

.3	Install wall trim around recessed locker banks.

.4	Install filler panels [and false fronts] where indicated and where obstruction occur.

.5	Install finished [end] [back] panels to exposed [ends] [back] of locker banks.

.6	Provide metal end panels and fillers to suit building openings.

END OF SECTION