Section Cover Page

Section 12 22 13 2011-08-26 Window Drapery and Accessories

Refer to “LEED Notes and Credits” page for additional guidance for LEED projects. Delete LEED items if project: .1 is excluded by the Department’s policy on LEED, or .2 the Department has determined that the work of this Contract is not to attain a LEED rating.

This Master Specification Section contains:

.1	This Cover Sheet

.2	LEED Notes and Credits

.3	Specification Section Text:

1.	General

1.1	Related Work Specified in Other Sections

1.2	References

1.3	Quality Guidelines

1.4	Submittals

1.5	Protection

1.6	Site Examination

1.7	Delivery

1.8	Waste Management and Disposal

2.	Products

2.1	Materials

2.2	Drapery Track or Rodding

2.3	Lined Drapery

2.4	Unlined Drapery

2.5	Drapery - General

2.6	Fabric Panels

3.	Execution

3.1	Drape and Track Installation

LEED Notes:

N/A

LEED Credits:

Contribution towards LEED credits in this section may apply as follows:

1.	LEED Credit MR 4: Recycled Content:

.1	The criteria is that the sum of post-consumer recycled content plus one-half of the pre-consumer content constitutes at least the percent (10% and 20%) of the total value of the materials in the project. Steel, aluminum and HPDE Plastics may have some recycled content. The manufacturers will need to provide information sheets demonstrating recycled content.

2.	MR Credit 5 Regional Materials:

.1	Use building materials or products that have been extracted, harvested, recovered and processed within 800 km (2400 km is shipped by rail or water) of the final manufacturing site.  Demonstrate that the final manufacturing site is within 800 km (2400 km is shipped by rail or water) of the project site for these products. The contractor will be required to submit documentation consisting of cost, weight, transportation service and distances as evidence of compliance with credit requirements.

3.	LEED Credit EQ 8.1: Daylight and Views: Daylight

.1	Provide building occupants a connection between indoor spaces and outdoor spaces by providing daylight in at least 75% of the regularly occupied spaces.

4.	LEED Credit EQ 8.2: Daylight and Views: Views

.1	Provide building occupants a connection between indoor spaces and outdoor spaces by providing direct line of sight to the outdoors in 90% of all regularly occupied spaces.

1.	General

1.1	RELATED Work Specified in Other SECTIONS

.1	[LEED Submittal Forms	Section 01 32 16]

.2	[LEED Requirements	Section 01 35 18]

.3	[Environmental Procedures	Section 01 35 20]

.4	Waste Management and Disposal	Section 01 74 19.

.5	[Vertical Louvre Blinds:	Section 12 21 16].

.6	[[Wood] [Metal] valance]:	[Section [06 20 00][            ].

1.2	REFERENCE DOCUMENTS

.1	Aluminum Association (AA):

| .1 | AA DAF-45-2003 | Designation System for Aluminum Finishes - 9th Edition |
| --- | --- | --- |

.2	American Society for Testing and Materials (ASTM):

| .1 | ASTM D1784-08 | Standard Specification for Rigid Poly (Vinyl Chloride) (PVC) Compounds and Chlorinated Poly (Vinyl Chloride) (CPVC) Compounds |
| --- | --- | --- |

.3	Canada Green Building Council (CaGBC):

| .1 | LEED Canada 2009 Rating System | LEED Canada for New Construction and Major Renovations. LEED Canada for Core and Shell Development. Website: www.cagbc.org] |
| --- | --- | --- |

1.3	QUALITY GUIDELINES

.1	The dimensional information on the attached Drapery Requirements Schedule is given to assist the bidder in assessing the scope of the work.  Dimensions must not be used for fabrication.

.2	Printed or patterned fabrics shall have repeats completely matched.

.3	All drapery fabrics and linings shall be inherently flame and burn resistant material in accordance with the Alberta Fire Marshall's regulations.

.4	CGSB 4-GP-152Ma - Drapes.

1.4	submittals

.1	Comply with requirements of Division 01.

.2	Submit samples of track and material in manufacturer's standard colour range for selection by the Minister.

.3	Submit product data indicating component thicknesses, finishes, and operators.

.4	Shop Drawings: Indicate dimensions in relation to window jambs, operator details, head [and sill] [conditions between adjacent materials] [corner conditions] anchorage details, hardware and accessories details.

SPEC NOTE: Delete LEED submittal item if project is not to attain LEED certification or if Credit MR 4 is not being sought.

.5	LEED Submittals: submit LEED submittal forms for Credit MR 4 in accordance with Section 01 32 16 LEED Submittal Forms and Section 01 35 18 LEED Requirements and the following:

.1	Documentation identifying quantity by weight of recycled content in products.

SPEC NOTE: Delete LEED submittal item if project is not to attain LEED certification or if Credit MR 5 is not being sought.

.6	LEED Submittals: submit LEED submittal forms for Credit MR 5 in accordance with Section 01 32 16 LEED Submittal Forms and Section 01 35 18 LEED Requirements and the following:

.1	Regional Materials: provide evidence that project incorporates required percentage [20] [30] % of regional materials/products, showing their cost, distances from extraction to manufacture and manufacture to project site, and total cost of materials for project.

1.5	PROTECTION

.1	Protect from damage drapery materials and accessories in all phases of handling, fabrication and installation.

.2	Protect from damage all building components during installation.

.3	In the event of damage, repair and make good of no additional expense to the contract.

1.6	SITE EXAMINATION

.1	The sizes indicated in the Drapery Requirement Schedule are based on information available when the Schedule was prepared.  Sizes indicate approximate measurement of finished drape.

.2	Accurate measurements must be made at the site before fabrication.  The building's structural characteristics are to be noted and allowances made for any additional supports, drapery material and track required.  Allowances must also be made for final on-site inspection and adjustments.  All sizes are approximate and to be used for estimating purposes only.   The Contractor shall be responsible in all cases for measurements.

1.7	DELIVERY

.1	Deliver to site at time of drapery installation, tagged as per item schedule.

1.8	waste management and disposal

.1	Separate and recycle waste materials in accordance with Section 01 74  19 Waste Management and Disposal and with the Waste Reduction Workplan.

2.	Products

2.1	MATERIALS

.1	Supply and install all fabric, traverse sets, tracks, hooks, fitments, hardware, weights, etc., which are necessary to complete the installation, unless specified to use existing hardware.

.2	Lining:  [Pride of Paris Roc-lon flame ban], [ivory], unless otherwise specified.

.3	Drapery Fabric, content, colour and pattern as follows:

SPEC NOTE:  Describe drapery fabric selection in preceding.

2.2	DRAPERY TRACK OR RODDING

.1	Standard (1):  Where indicated as Standard on the Drapery Requirements Schedule, the track shall be a "cut to measure, heavy duty centre-close, two-way draw" enclosed track.  Finish white.  Ceiling or wall mount track.  [Kirsch No. 9813], [Eastern No. 2701] rodding sets.  Tracks shall be complete with all necessary accessories including adequate slides, overlap corners, draw cords, wall projection brackets, pulleys, etc.  Tension pulleys to be used, [Kirsch No. 9924].  Finish white.  Tracks used must be of heavy duty construction.

.2	I-BEAM (2):  Where indicated as I-Beam on the Drapery Requirements Schedule, the track shall be [Lilo No. 10] heavy duty steel, "enamel finish", cut to measure track, [Eastern "Star" I-Beam rail].  All tracks shall be complete with all necessary accessories, include adequate rollers, end stops, etc.

.3	Special (A):  Where indicated as Special A on the Drapery Schedule, the track shall be [Kirsch No. 9046] hand traverse, ceiling mounted Architrac, extruded, 1.27 mm, high strength, extruded aluminum alloy single channel track, [Eastern No. 2707].

.4	Special (B):  Where indicated as Special B on Drapery Schedule, the track shall be [Kirsch Paneltrac] complete with precut sliders and one side of ["Velcro"] fastening tape attached, precut aluminum weight strips for bottom hem insertion, pile side of [Velcro] for panel headings and including all necessary accessories including end stops etc.

.5	Special (C):  Where indicated as C on Drapery Schedule, use a Roman blind.  A finished hardwood leader, approximately 25 x 38 mm shaped to accept a [Velcro] tape heading to top surface and screw eyes to underside of Header to be screwed to wall or in case of a recessed window, within the window recess as specified.  Pile side of [Velcro] tape to be applied to blind heading.  Valance, if any to be specified in schedule.  Blinds to be lined, unlined as per Drapery Schedule.  Side seams to be blind stitched.

A flat 10 mm aluminum or brass strip to be sewn into concealed pocket 100 mm above bottom edge of blind.  Bottom 125 mm of blind to be lined with face fabric bottom edge finished straight unless specified as shaped in Drapery Schedule.

Plastic rings spaced at 150 mm vertically and 380 mm horizontally to be securely sewn to back of blind.  Nylon cord knotted to bottom rings and run continuous to tie-off cord fitted with a [#25 Lilo] cord weight with rubber bumper to be used.  Drawing cord to pull over wall-mounted pulley and be secured at wall-mounted awning cleat.

2.3	LINED DRAPERY

.1	Lining to be sewn to face fabric on top and both sides of each drape.

.2	Face fabric return not less than 25 mm.

.3	Lining to be hemmed 25 mm shorter than face fabric.  Hem shall be free hanging.

.4	Drapes shall not be less than double fullness or with widths as specified.

2.4	UNLINED DRAPERY

.1	Fabrics without selvages to have zigzag stitched flat seams.

.2	Selvages of casements to be trimmed, serged and flat sewn along seams.

.3	Hems and headings to be double and not less than 100 mm.

.4	Drapes shall not be less than two and one-half (2 1/2) fullness.

2.5	DRAPERY-GENERAL

.1	Drapes shall be weighted at corners and side seams or shall be continuously weighted with a chain, [as necessary].

.2	Hems shall be machine blind stitched in matching thread of a suitable weight and fibre and flat sewn for best appearance on either side of the drape.  All ends shall be tied off and hems shall be perfectly straight.  Invisible thread not to be used.

.3	Headings shall be stiffened with woven buchram or washable pellon.  Headings to have 3 fold pinched pleats with each pleat tacked top and bottom.

.4	For standard traverse French pleat draperies use "pin-on" type hooks and "sewn-on" end bottom.

.5	Half and full width panels only may be used.  Half width panels shall occur on the outside of each drape and not at the centre.

.6	All drapery shall be centre drawn unless otherwise specified.

.7	Each drape shall be supplied with a permanent sew-in label(s) indicating fabric content and the appropriate CAN/CGSB-86.1-M91 Care Labelling of Textiles.

.8	Refer to drapery track or rodding for specific specifications.

.9	Contractor to consult the Minister before fabrication.

2.6	FABRIC PANELS

.1	Material to be uniformly stretched over 12 x 44 mm wood frame to meet overall dimensions and stapled evenly and firmly on backside of frame so staples are not visible to finished surfaces.  Frame to be reinforced with angle brackets at each inside corner.  Hooks to be centred on back side of top of frame.

.2	All fabrics to be centred horizontally and vertically with full pattern repeats centred whenever possible.

3.	Execution

3.1	DRAPE AND TRACK INSTALLATION

.1	Work shall be executed only by skilled tradesmen.

.2	Prior to installation, draperies shall be pressed to eliminate creases and wrinkles.  Drapes shall be gathered into loose pleats, tied with tape at top, centre and bottom and hung for a minimum of 48 hours.

.3	Install in accordance with manufacturer's specifications, i.e. the correct number of screws, projection brackets, supports, etc.  There shall be no unsupported length over 900 mm.  Where filing or hand drawn, a centre support will be required if track is more than 600 mm long.

.4	All tracks shall be installed using the necessary screws, plugs, toggle bolts, anchors or rawlnuts necessary to produce a heavy duty installation permitting no loosening of brackets, tracks or other operating parts when subject to extensive use.

.5	Drapes shall be hung from [ceilings], [soffits], [or] [walls] as specified.

.6	Hems shall be perfectly straight and drape shall hang in uniform pleats.

.7	Care to be taken with textured ceilings and/or painted surfaces when mounting tracks.

.8	Allow for a 150 mm stackback clearance near doors.

END OF SECTION