Section Cover Page

Section 02 92 19 Removal and Disposal of 2024-06-18 Miscellaneous Chemicals

Use this section to specify the removal and disposal of miscellaneous chemicals.

This Section may be used as part of a renovation contract or as part of a contract directly with a hazardous waste disposal contractor.  Edit this Section to suit contracting option selected.

This Technical Specification Section contains:

.1	This Cover Sheet

.2	Specification Text

1.	General

1.1	Section Includes

1.2	Removal Contractors Qualifications

1.3	Disposal Contractor Qualifications

1.4	Regulatory Requirements

2.	Products

Not Used

3.	Execution

3.1	Miscellaneous Chemical

3.2	Transportation and Permanent Disposal

3.3	Schedule of Miscellaneous Chemicals

1.	General

1.1	SECTION INCLUDES

.1	This Section includes requirements for identification, removal, preparation for disposal, transportation, and permanent disposal of the miscellaneous chemicals.

1.2	REMOVAL CONTRACTOR QUALIFICATIONS

.1	Persons employed for the removal of the miscellaneous chemicals must be competently trained in the handling and safe work procedures to do so.

1.3	DISPOSAL CONTRACTOR QUALIFICATIONS

.1	Handling and transportation of miscellaneous chemicals shall be performed by a hazardous waste company in compliance with the Environmental Protection and Enhancement Act.

.2	Carrier of hazardous wastes shall have successfully completed a Transportation of Dangerous Goods course acceptable to the authority having jurisdiction within the past three years.

1.4	REGULATORY REQUIREMENTS

.1	Comply with the following:

.1	Environmental Protection Act, (1999) (Canada).

.2	Environmental Protection and Enhancement Act, (2023) (Alberta).

.3	Occupational Health and Safety Act (2021), Regulation (2021) and Code (2023) (Alberta).

.4	Transportation of Dangerous Goods Act, (1992) (Canada).

.5	Dangerous Goods Transportation and Handling Act (2021) and Regulations (1997) (Alberta)

.6	Other legislation and regulations which apply to the performance of asbestos control work.

1.5	HANDLING AND WORKER PROTECTION

.1	Wear chemical resistant gloves in addition to other site specific personal protective equipment.

.2	Provide workers with additional chemical protective clothing and other personal protective equipment where contact with the chemicals may occur. Provide clothing and equipment appropriate for the potential level of exposure.

2.	Products (Not Used)

3.	Execution

3.1	MISCELLANEOUS CHEMICALS

.1	Locate and remove the miscellaneous chemicals designated to be disposed of.

.2	Classify the miscellaneous chemicals based on chemical properties, quantity, and the type of hazard they present. Safely handle, package, transport, and dispose of the miscellaneous chemicals in accordance with the applicable regulations, guidelines and codes.

.3	Absorb any spill with absorptive material, immediately ventilate area and clean up the spill based on the chemical properties, quantity, and the type of hazard the chemical presents.

3.2	TRANSPORTATION AND PERMANENT DISPOSAL

.1	Transport waste miscellaneous chemicals in accordance with the Alberta and Federal legislation and regulations and local landfill requirements

.2	Ensure that all materials are properly packaged and labeled prior to transportation.

.3	Use an approved hazardous waste company to transport and permanently dispose of miscellaneous chemicals.

.4	Transport hazardous waste materials in properly placarded vehicles.

.5	Each load shall be accompanied by a properly completed Transportation of Dangerous Goods Regulation (TDGR) Waste Manifest.  Provide the [Province] [Environmental Consultant] with a copy of each shipping document and waste manifest.

.6	Dispose of, or recycle miscellaneous chemicals off-site in accordance with Local, Provincial, and Federal requirements.

3.3	SCHEDULE OF MISCELLANEOUS CHEMICALS

SPEC NOTEs: Edit schedule to suit project requirements. The Contractor is ultimately responsible for the determination of total miscellaneous chemical quantities.

.1	Hazardous Chemicals: Type [  ]   Total [  ]

.2	Household Chemicals: Type [  ]   Total [  ]

.3	Aerosol Cans: Type [  ]   Total [  ]

.4	Empty Compressed Gas Cylinders: Tye [  ]   Total [  ]

END OF SECTION